Home Video Game Manual for the Bally Astrocade

Dave Nutting Associates

Text Release 2.1 - February 8, 2002

This document, officially called the 'Home Video Game System' manual, is better known as the 'Nutting' or 'DNA' manual.

Conventions:

1)  To match the original manual as closely as possible (for table of

contents reasons), two blanks lines separate each 'page.'  This

is followed by the page number and then one more blank line.

2)  The Page Number appears at the top of each page, not the bottom

(don't get confused); it takes up the first line.

3)  Every instance of the word 'cassette' has been replaced by the

word 'cartridge' to avoid any confusion with the BASIC Cassette

Interface (which isn't mentioned in this manual at all).

4)  Special Character Representations:

____  ____

a. IORQ, MREQ   = IORQ#, MREQ#

b. Subscripts   = '_' (underscore) - contextual

c. Superscripts = '^' (caret)      - contextual

d. The Greek symbol Phi ('O' over-striked with an 'I') is

replaced with the word 'Phi'

From the original manual:

This document and its contents are the property of Dave Nutting Associates,

incorporated and Bally Manufacturing Corporation.  The information contained

herein is both proprietary and confidential.

No part of this document may be reproduced, stored in a retrieval system, or

transmitted in any form or by any means electronic, mechanical, chemical,

photographical, recording, photocopying or otherwise.

Dave Nutting Associates, incorporated assumes no responsibility for the use of

any circuitry other than circuitry embodied in a Dave Nutting Associates,

incorporated designed product.

This document must be returned to Dave Nutting Associates, Incorporated by

registered mail within five days of written demand.

(c) 1978 Dave Nutting Associates, Incorporated

(c) 1978 Bally Manufacturing Corporation

This page intentionally left blank for double-sided print purposes

TABLE OF CONTENTS - SOFTWARE

----------------------------

1              Home Video Game System

2              User Program Interface

5              System Routine Conventions

7              Inline Argument Mask Table Entry

8    INTPC     Begin Interpreting

9    XINTC     Exit Interpreter

10    RCALL     Call Assembly Language Subroutine

11    MCALL     Call Interpreter Subroutine

12    MJUMP     Interpreter Jump

13    MRET      Return From Interpretive Subroutines

14              Screen Handler

15    SETOUT    Set Display Ports

16    FILL      Fill A Contiguous Area With Constant

17    RECTAN    Paint A Rectangle

18              Write Routines

19              Calling Sequence

20              Representation

21    VWRITR    Write Relative From Vector

22    WRITR     Write Relative

23    WRITP     Write With Pattern Size Scare Up

24    WRIT      Write Pattern

25    WRITA     Write Absolute

26    SAVE      Save Area

27    RESTOR    Restore Area

28    VBLANK    Blank From Vector

29    BLANK     Blank Area

30    SCROLL    Scroll Window

31              Alphanumeric Display Routines

34    DISNUM    Display BCD Number

35    DISTIM    Display Time

36    CHRDIS    Display Character

37    STRDIS    Display String

38              Interpretation of Codes 64H to 7FH

39              Vectoring - Vectoring Routines

42    VECT      Vector Object In Two Dimensions

43    VECTC     Vector A Co-ordinate

44    RELABS    Convert Relative Co-ordinates

45    RELAB1    Convert Relative Address To Absolute

46    COLSET    Set Color Registers

47    INCSCR    Increment Score And Compare To End Score

48    PAWS      Pause

49    KCTASC    Key Code to ASCII

50    SENTRY    Sense Transition

53    DOIT      Respond To Input Transition

54    PIZBRK    Coffee Break, Black Out Screen, Wait For Key

55              Example

56              Interrupt - Music Processor

57              MUZCPU Instruction Set

58              Music Score Example

59    BMUSIC    Begin Playing Music

60    EMUSIC    Stop Music

61    ACTINT    Active Interrupts

62    DECCTS    Decrement Counter/Timers

63    CTIMER

64    STIMER    Decrement Timers

65    MOVE      Move Bytes

66    INDEXN    Index Nibble

67    STOREN    Start Nibble

68    INDEXW    Index Word

69    INDEXB    Index Byte

70    SETB      Store Byte

71    SETW      Store Word

72              Cartridge Conventions

75    GETPAR    Get Game Parameter

76    MENU      Display Menu And Branch On Selection

77    GETNUM    Get Number

79    MSKTD     Joystick Mask To Deltas

80    RANGED    Ranged Random Number

TABLE OF CONTENTS - HARDWARE

----------------------------

81              Introduction

82              Memory Map

85              Screen Map

88              Color Mapping

89              Background Color

90              Vertical Blank

92              Interrupt Feedback

92              Interrupt Control Bits

93              Screen Interrupt

93              Light Pen Interrupt

94              Magic Register

95              Expand

96              Shifter

96              Flopper

98              Rotator

100              OR And XOR

100              Intercept

101              Player Input

103              Master Oscillator

104              Tones

104              Sound Block Transfer

106              Output Ports

107              Input Ports

109             Microcycler

111             Address Chip Description

114             Data Chip Description

117             I/O Chip Description

119             Music Processor

123             Custom Chip Timing

131             Video Timing

135             Electrical Specifications for

Midway Custom Circuits

LIST OF ILLUSTRATIONS

---------------------

6             Context Block Format

20             Pattern Representation

32             Option Byte

33             Alternate Font Descriptor

40             Vector Block

41             Vector Status Detail

41             Checks Mask Detail

44             Normal and Flopped Co-ordinate Systems

51             Keypad Mask Configuration

56             Voices Status Register

66             INDEXN

68             INDEXW

74             Cartridge Map.

78             Display Number Options

78             Character Display Options

83             Memory Map Low Resolution

84             Memory Map High Resolution

86             Screen Map Low Resolution

87             Screen Map High Resolution

91             Color Register Map

97             Shifter - Flopper

99             Rotator

102             Player Input

105             Audio Generator Block Diagram

106             Output Ports

107             Input Ports

108             System Block Diagram

110             Microcycler Block Diagram

113             Address Chip Block Diagram

116             Data Chip Block Diagram

118             I/O Chip Block Diagram

121             Master Oscillator

122             Tone Generators

124             Memory Write Without Extra Wait State

125             Memory Write With Video Wait State

126             Memory Read Without Extra Wait State

127             Memory Read With Video Wait State

128             I/O Read From Port 10H - 17H

129             I/O Read From Other Than Port 10H - 17H

130             I/O Write

132             Relationship Between 7M, Horiz Dr, Vert Dr,

Phi G, PX# and RAS

133             Relationship Between Horiz Dr, Horiz Blank,

Horiz Sync, and Color Burst

134             Relationship Between Vertical Sync,

Vertical Blank, and Vertical Drive

This page intentionally left blank for double-sided print purposes

HOME VIDEO GAME SYSTEM

----------------------

This documentation describes the Bally Home Video Game System.  The

description begins with a discussion of the major sub-sections of the

system.  Following this, each sub-section is presented in greater

detail, with detailed particulars, such as calling sequences and

resource use.

The major sub-sections of the system are:

The User Program Interface - Allows cartridges to reference the

system routines through a standard interface.  Includes an interpreter.

The Screen Handler - A complex of routines for creating screen images.

Includes facilities for initialization, pattern and character display,

co-ordinate conversion, and object vectoring.

The Interrupt Processor - Decrements timers, plays music, and

produces sounds.

The Human Interface - Reads keyboard and control handles, inputs game

selection and options.

Math Routines - A package of routines for manipulating floating

BCD numbers.

USER PROGRAM INTERFACE

----------------------

The User Program Interface (UPI) is a set of procedures and conventions,

which are utilized by a cartridge program to access the facilities

provided by the home video game system.  By adhering to these conventions

a cartridge program will be system independent, thus allowing improvements

to be made to later versions of the system and on board games, while

maintaining upward compatibility.

The basic rule for using the UPI is:

With exception to the system DOPE vector, no cartridge

should ever address system ROM directly, or expect a

given cell to always equal a certain value.

The mechanism for calling a system routine is:

RST     56

DEFB    (routine # + option)

where routine number is an even number specifying which sub-routine

to transfer to, symbolic identifiers, which are equated to routine

numbers, are provided by HVGLIB.

Option is used to specify how arguments are being passed to the

system routine.  If option equals zero, the arguments are presumed to

exist in CPU registers; if option equals 1, the arguments are taken

to follow in line after the routine number/option byte.  These arguments

are loaded into the CPU registers automatically before the

called routine is entered.  The arguments required by each system

routine are given in the routine's detail documentation.

The SYSTEM macro generates the sequence previously mentioned

with option = 0:

SYSTEM  (routine #)

(example)

SYSTEM  FILL

The SYSSUK macro generates the sequence previously mentioned

with option = 1.

SYSSUK  (routine #)

Frequently it is desirable to string several system routine calls

together.  If four or more calls follow in sequence, it is more

efficient to utilize the interpreter.  By using the interpreter we

void the overhead of the RST 56 instruction by expecting a call index

to immediately follow the call index or arguments used in the previous

system routine.

Special call indexes are used to enter and exit interpretive mode:

Example:

SYSTEM  INTPC        ;BEGIN INTERPRETING

DO      FILL         ;DO FILL ROUTINE

DEFW    NORMEM       ;STARTING AT TOP OF SCREEN

DEFW    92*BYTEPL    ;CONTINUING FOR 92 LINES

DEFB    0            ;FILLED WITH ZEROES

DO      CHRDIS       ;DO CHARACTER DISPLAY ROUTINE

DEFB    0            ;Y-AXIS POSITION

DEFB    10           ;X-AXIS POSITION

DEFB    8            ;OPTIONS-PLOP,10-ON,00-OFF

DEFB    'A'          ;CHARACTER TO BE DISPLAYED

EXIT                 ;EXIT INTERPRETER

A block of call indexes have been set aside for the internal use of

cartridge programs.  If a negative call index is encountered, the

user's macro routine address table and argument table are utilized.

The user is responsible for storing the addresses of these tables

into dedicated system RAM cells.

All UPI routines are re-entrant.

Registers which are not defined as containing output parameters

will not change.

SYSTEM ROUTINE CONVENTIONS

--------------------------

A system routine is coded like a conventional machine language

subroutine, with the exception that output parameters are not passed

through registers, but rather through the context block.

The context block is created by the RST 56 call.  The user's register

set (AF, BC, DE, HL, IX, IY) is pushed onto the stack.  Register IY

is set to point at this stack frame.  Thus a copy of the input

arguments exists in RAM which the system routine may refer to as needed.

These arguments are also present in the registers when the system

routine is entered; hence it is only necessary to refer to the context

block when one has clobbered an input argument.

An output argument is returned to the caller by setting it in the

context block.  If a register was changed, but the associated cell in

the context block was not, then the register will have its old value

on return.  Thus a system routine is free to use any of the registers

it needs without concern to saving and restoring.  Moreover, the user

can assume that no registers will change except those defined as

returning an output argument.

The following illustration describes the context block and equates

provided in HVGLIB for each field.

Four tables are used by the UPI in the control transfer process.  The

first two tables give the routines starting address indexed via call

number.  The systems table is called SYSDPT.  The user may extend this

table by storing the address of his extended table into USERTB,

USERTB+1.  This address should point 128 bytes before the first entry.

The other two tables describe what in line arguments a call that

specifies in line arguments should expect.  This table gives a one-byte

bitstring, also indexed via call number.  The systems name is MRARGT,

the user's address is in UMARGT, UMARGT must point 64 bytes ahead.

Arguments must follow the call in a specified order.

Note that the context contains additional information not shown.  This

information exists both above and below the context.  User programs

should never use this information or even assume that it exists.  The

user should only address this area by using IY.

+--------------+-------------+-------------+

| DISPLACEMENT | MEMORY CELL | EQUATE NAME |

+--------------+-------------+-------------+

|      0       |     IY      |    CBIYL    |

+--------------+             |             |

|      1       |             |    CBIYH    |

+--------------+-------------+-------------+

|      2       |     IX      |    CBIXL    |

+--------------+             |             |

|      3       |             |    CBIXH    |

+--------------+-------------+-------------+

|      4       |     E       |      CBE    |

+--------------+-------------+-------------+

|      5       |     D       |      CBD    |

+--------------+-------------+-------------+

|      6       |     C       |      CBC    |

+--------------+-------------+-------------+

|      7       |     B       |      CBB    |

+--------------+-------------+-------------+

|      8       |   FLAGS     |    CBFLAG   |

+--------------+-------------+-------------+

|      9       |     A       |      CBA    |

+--------------+-------------+-------------+

|      A       |     L       |      CBL    |

+--------------+-------------+-------------+

|      B       |     H       |      CBH    |

+--------------+-------------+-------------+

CONTEXT BLOCK FORMAT

IN LINE ARGUMENT MASK ENTRY

---------------------------

TABLES MRARGT AND UMARGT

------------------------

If a bit corresponding to a register is set, the register is loaded.

The order in which the arguments must appear is:

IX (L then H), E, D, C, B, A, L, H

If an argument isn't specified, it is omitted.

7   6   5   4   3   2   1   0

+---+---+---+---+---+---+---+---+

| H | L | A |IX | B | C | D | E |

+---+---+---+---+---+---+---+---+

UPI INTPC

BEGIN INTERPRETING

Calling Sequence:       SYSTEM  INTPC

Arguments:              NONE

Notes:                  NONE

Description:

See UPI description for explanation of interpreter.

UPI XINTC

EXIT INTERPETER

Calling Sequence:       EXIT

Arguments:              NONE

Description:

This code causes the interpreter to exit.  Execution of machine

instructions proceeds at the following location.

Restrictions:

This routine should only be called using the interpreter.  A direct

system call would produce unpredictable (and catastrophic) results.

UPI RCALL

CALL ASSEMBLY LANGUAGE SUBROUTINE

Calling Sequence:       DO     RCALL

or

DONT   RCALL

DEFW   (routine address)

Arguments:              HL = address of routine to call

Description:

RCALL may be used to call any assembly language subroutine from the

interpreter.  When the subroutine returns, interpretation proceeds

at the next instruction.

When the assembly language routine receives control, HL will point

at the routine's starting address, the other registers will contain

their current values.  Any changes made to the register set by the

subroutine will not be passed along.  To pass an output parameter, the

subroutine must alter the context block, which is pointed to by IY.

Restrictions:

Assembler routines must not destroy IY.

Example:                DEFB     RCALL

DEFW     CLRAC

.

.

.

CLRAC:  XOR      A

RET

UPI MCALL

CALL INTERPRETER SUBROUTINE

Calling Sequence:       SYSTEM  MCALL

or

SYSSUK  MCALL

DEFW   (routine address)

Arguments:              HL = Subroutine address

Description:

MCALL is used to call an interpreter sequence in a subroutine.  MCALL

may be used from machine language as well as within an interpreted

sequence.  Calls may be nested infinitely, limited only by stack

space (4 bytes per call).

To exit the interpreted subroutine, use MRET

Example:                SYSSUK  MCALL

DEFW    ZAPALL

.

.

.

ZAPALL: DO      FILL+1         ;DO FILL

DEFW    NORMEM

DEFW    0FFFH

DEFB    0

DO      MRET           ;GO BACK TO CALLER

UPI MJUMP

INTERPRETER JUMP

Calling Sequence:       DO      MJUMP

or

DONT    MJUMP

DEFW   (Goto address)

Arguments:              HL = Go to address

Description:

The current interpretive program counter is set to the contents of HL.

The next instruction is fetched from that address.

Restrictions:

MJUMP must be called from the interpreter. The targets of all JUMPS

must also be interpreted sequences.

Example:                SYSTEM  INTPC          ;ENTER INTPC STEP

.

.

.

DO      MJUMP          ;JUMP TO END OF

DEFW    END            ;INTPC STEP

.

.

.

END:    DEFB    XINTC          ;EXIT INTERPRETER

UPI MRET

RETURN FROM INTERPRETIVE SUBROUTINES

Calling Sequence:       DO      MRET

Arguments:              None

Description:

MRET causes execution to proceed at the instruction following the

corresponding MCALL instruction.  See MCALL for more information.

SCREEN HANDLER

--------------

The screen handler is a group of routines for generating frame buffer

images.  Included are entries for filling sections of the screen with

constant data, the animation of figures, and the display of alpha-

numerics.

Many of these routines utilize the MAGIC functions provided by the

custom chips.  Since the status of these chips cannot be context-

switched, many of these routines are not re-entrant.  The user is

responsible for preventing conflicts.  This can be done by disabling

interrupt, or implementing a semaphore.

SCREEN SETOUT

SET DISPLAY PORTS

Calling sequence:       SYSTEM  SETOUT

or

SYSSUK  SETOUT

DEFB    BLINE*2

DEFB    HORIZX/4

DEFB    INMOD

Arguments:              A  = Data to output to INMOD  (port EH)

B  = Data to output to HORCB  (port 9H)

D  = Data to output to VERBL  (port AH)

Output:                 None

Description:            Outputs above data to ports

See hardware writeup for discussion of

above ports.

SCREEN FILL

FILL A CONTIGUOUS AREA WITH CONSTANT

Calling Sequence:       SYSTEM  FILL

or

SYSSUK  FILL

DEFW    (first byte)

DEFW    (number of bytes)

DEFB    (data to fill with)

Arguments:              A  = Data to fill with

BC = Number of bytes to fill

DE = Address to begin filling at

Description:

This routine sets the memory range DE to (DE+BC-1) to the

specified constant.

Notes:

Fill can be used for screen clearing, or initialization of scratchpad

RAM.  It is re-entrant.

SCREEN RECTAN

PAINT A RECTANGLE

Calling Sequence:       SYSTEM  RECTAN

or

SYSSUK  RECTAN

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (X size)

DEFB    (Y size)

DEFB    (color mask)

Arguments:              A  = Color mask to write rectangle with

B  = Y-size of rectangle in pixels

C  = X-size of rectangle in pixels

D  = Y co-ordinate for UL corner of rectangle

E  = X co-ordinate for UL corner of rectangle

Description:

A rectangle of specified size of color mask is written at X,Y.  RECTAN

uses the MAGIC functions and is not re-entrant.

Example:                Put up a 3 X 4 rectangle of color 2 at 15,13.

DO      RECTAN

DEFB    15

DEFB    13

DEFB    3

DEFB    4

DEFB    10101010B

SCREEN WRITE ROUTINES

---------------------

Virtually every video game involves the manipulation of animated

figures.  These figures are composed of patterns which are arbitrary

pixel arrays.  The write routines are used to transfer such patterns

to the screen.

Five hierarchical levels of call are supported.  The levels differ in

the amount of preprocessing required by the user before calling.  The

highest level assumes that most of the parameters reside in a standard

data structure, while the lowest level presumes that all arguments are

in registers with all attendant transformations (such as relative-to-

absolute conversion) already accomplished.  The five levels are:

(1)     Write from a Vector

(2)     Write Relative

(3)     Write Variable Pattern

(4)     Write

(5)     Write Absolute

Two transformations of the pattern may be performed prior to writing.

They are FLOP and EXPAND.  FLOP is mirroring the pattern on the X-axis.

EXPAND is the translation of a 1-bit per pixel pattern into a 2-bit per

Pixel pattern.  Since many patterns are only two-color, this allows for

more efficient pattern storage.  FLOP and EXPAND can both be done at

the same time.

Three writing modes may be used.  They are PLOP, OR, and XOR.  PLOP is

a conventional store into RAM.  If OR is optioned, the data being written

is ORed bit by bit with whatever was already there.  Similarly, if XOR

is set, the pattern is XORed with that beneath. Use of OR or XOR takes

slightly longer since a read before write must be performed.

Note that ROTATE is not currently supported in software due to

space considerations.

STANDARD CALLING SEQUENCE

-------------------------

Every write routine uses a subset of the following argument/register

assignment:

A  = Magic Register

B  = Y Pattern Size

C  = X Pattern Size in Bytes

D  = Y Co-ordinate (0 - 101)

E  = X Co-ordinate (0 - 159)

HL = Pattern Address

IX = Vector Address

PATTERN REPRESENTATION

----------------------

The higher the level of the write routine, the more ancillary infor-

mation is stored with the pattern.  The following diagram shows what

each level expects.  Any bytes of lower address than the pointer for

a given level, need not be specified.

Use Restrictions:

None of the write routines are re-entrant due to Magic Register/Expander

clobber.

+----------------+

VWRITR,WRITR -->  | X DISPLACEMENT |  0

+----------------+

| Y DISPLACEMENT |  1

+----------------+

WRITP -->  |     X SIZE     |  2

+----------------+

|     Y SIZE     |  3

WRIT,WRITA -->  +----------------+

|                |  4

+----------------+

|                |

.                .

.                .

|                |

+----------------+

|                |  N+4

+----------------+

SCREEN WRITE  VWRITR

WRITE RELATIVE FROM VECTOR

Calling Sequence:       SYSTEM  VWRITR

or

SYSSUK   VWRITR

DEFW     (vector)

DEFW     (pattern)

Arguments:              HL = Pattern address

IX = Vector Address

Output:                 DE = Absolute address used

A  = Magic register used

Description:

The co-ordinates and magic register are loaded from the specified

vector.  (See vector routine document)  The relative co-ordinates

stored with the pattern are added to the co-ordinates from the vector.

The pattern size is also taken from the pattern and writing proceeds.

Notes:

If expansion is to be done, the ON/OFF color must be set by the user

before calling VWRITR.

SCREEN WRITE  WRITR

WRITE RELATIVE

Calling Sequence:       SYSTEM  WRITR

or

SYSSUK  WRITR

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (Magic Register)

DEFW    (Pattern address)

Arguments:              HL = Pattern address

A  = Magic Register

D  = Y co-ordinate

E  = X co-ordinate

Output:                 DE = Screen Address Used

A  = Magic Register Used

Description:

The relative co-ordinates stored with the pattern are added to the

co-ordinates passed in DE.  Pattern size is taken from the pattern.

Notes:

If expansion is to be done, the ON/OFF color must be set by the user

before calling WRITR.

SCREEN WRITE   WRITP

WRITE WITH PATTERN SIZE SCARE UP

Calling Sequence:       SYSTEM  WRITP

or

SYSSUK  WRITP

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (Magic Register)

DEFW    (Pattern address)

Arguments:              HL = Pattern Address

A  = Magic Register

D  = Y co-ordinate

E  = X co-ordinate

Output:                 DE = Screen Address Used

A  = Magic Register Used

Description:

The pattern size is taken from the pattern.

Notes:

User must worry about ON/OFF color if expansion is used.

SCREEN WRITE   WRIT

WRITE PATTERN

Calling Sequence:       SYSTEM  WRIT

or

SYSSUK  WRIT

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (X pattern size)

DEFB    (Y pattern size)

DEFB    (Magic Register)

DEFW    (Pattern address)

Arguments:              HL = Pattern Address

A  = Magic Register to use

B  = Y pattern size

C  = X pattern size

D  = Y co-ordinate

E  = X co-ordinate

Output:                 DE = Absolute address used

A  = Magic Register used

Notes:

User must set ON/OFF color if using expansion.

SCREEN WRITE   WRITA

WRITE ABSOLUTE

Calling Sequence:       SYSTEM  WRITA

or

SYSSUK  WRITA

DEFW    (Absolute address)

DEFB    (X pattern size)

DEFB    (Y pattern size)

DEFB    (Magic Register)

DEFW    (Pattern address)

Arguments:              HL = Pattern Address

A  = Magic Register

B  = Y Pattern size

C  = X Pattern size

DE = Absolute screen address of upper left-

hand corner of where to write

Notes:

This entry can be used for pattern writing to non-magic memory.

The value in A is not output to (MAGIC); it is only interrogated

to decide whether to FLOP or EXPAND.

SCREEN SAVE

SAVE AREA

Calling Sequence:       SYSTEM  SAVE

OR

SYSSUK  SAVE

DEFW    (save area)

DEFB    (X size)

DEFB    (Y size)

DEFW    (Screen address)

Arguments:              B  = Y size of area to save

C  = X size of area to save (in bytes)

DE = Address of save area

HL = Absolute address of upper left-hand corner

of area to save

Description:

SAVE is used to preserve what is 'underneath' a moving pattern.  SAVE

copies the indicated area of the screen to the save area.  The sizes of

the area which were saved is preserved in the first two bytes of the

save area.

The save area size must be greater than or equal to the X-size times the

Y-size plus 2.

The save area may be MAGIC or non-MAGIC.

SCREEN RESTORE

RESTORE AREA

Calling Sequence:       SYSTEM  RESTOR

or

SYSSUK  RESTOR

DEFW    (Save area)

DEFW    (Screen address)

Arguments:              DE = Save area to restore from

HL = Absolute address of upper left-hand corner

of area to restore

Description:

RESTORE is the inverse of SAVE.  The size of the area to restore is

taken from the first two bytes of the save area.

SCREEN  VBLANK

BLANK FROM VECTOR

Calling Sequence:       SYSTEM  VBLANK

or

SYSSUK  VBLANK

DEFW    (Vector address)

DEFB    (X size)

DEFB    (Y size)

Arguments:              D  = Y size

E  = X size (in bytes)

IX = Vector address

Description:

The BLANK bit in the vector status byte is tested.  If it is not set,

no blanking is done.  If it is set, it is reset, then the old screen

address is taken from the vector and blanking is done.  If FLOPPED is

specified by the Magic Register byte in the vector, a flopped blank is

done.  VBLANK always blanks to zero.

SCREEN  BLANK

BLANK AREA

Calling Sequence:       SYSTEM  BLANK

or

SYSSUK  BLANK

DEFB    (X size)

DEFB    (Y size)

DEFB    (Blank to)

DEFW    (Blank address)

Arguments:              HL = Blank address (not MAGIC)

B  = Data to blank to

D  = Y size

E  = X size

Description:

The specified area is blanked to whatever is passed in B.

SCREEN SCROLL

SCROLL WINDOW

Calling Sequence:       SYSTEM  SCROLL

or

SYSSUK  SCROLL

DEFW    (line increment)

DEFB    (# of bytes)

DEFB    (# of lines)

DEFW    (first byte)

Arguments:              B  = Number of lines to scroll

C  = Number of bytes on line to scroll

DE = Line increment

HL = First byte to scroll

Description:

This routine copies NBYTES from first line +INC to first line.

Thus to scroll upward, HL points at the first line (which is over-

written) and the line increment would be positive.  To scroll downward

HL points at the last line and the line increment would be negative.

The value in HL is an absolute address calculated by:

BASE OF SCREEN + #BYTES IN X OFFSET +(#lines offset*byte per line)

Note:

This routine can only be used to scroll one line at a time.

SCREEN ALPHANUMERIC

ALPHANUMERIC DISPLAY ROUTINES

HVGSYS provides several routines for the display of alphanumeric

information.  This section provides information which is common

to all of the alphanumeric display routines.

The ASCII character code is used to represent all strings with

the following extensions:

Characters with hex equivalents in the range 1 - 1F are

interpreted as tabulation codes which cause the character

display routines to skip over N character positions before

writing the following characters.

The characters 20H to 63H are displayed as 5 X 7 standard

graphics with 3 pixels of horizontal spacing and 1 pixel

of vertical spacing.

The characters between 64H and 7FH are interpreted by STRDIS

as control codes which cause the contents of registers C, DE,

and IX to be changed to the value that follow the string.

See table accompanying STRDIS.

The characters between 80H and FFH are taken as references to

a user supplied alternate character font.

The following argument/register combinations are used by all of the

alphanumeric display routines.

Register C contains the options byte formatted as shown below.

ENLARGE FACTOR specifies if the character is to be enlarged in size.

The table below defines the possible values for this parameter.

XOR/OR WRITE - All writes are performed through magic memory.  Use

of one of these options causes the character to be ORed/XORed with

what was beneath it.

ON/OFF COLOR - All characters are stored one bit per pixel, but are

written two bits per pixel by use of the expander.  This field specifies

the pixel values to translate the one bit per pixel representation into.

For example, the value 1101 specifies that the foreground color is 11,

and the background color is 01.

OPTION BYTE

+------+------+------+------+------+------+------+------+

|   ENLARGE   | XOR  |   OR |      ON     |     OFF     |

|   FACTOR    |WRITE | WRITE|    COLOR    |    COLOR    |

+------+------+------+------+------+------+------+------+

ENLARGE       HOW MANY        ENLARGED SIZE

FACTOR      TIMES LARGER     OF SINGLE PIXEL

00             1                1 X 1

01             2                2 X 2

10             4                4 X 4

11             8                8 X 8

D Register contains the Y co-ordinate and the E register contains

The X co-ordinate.  These co-ordinates give the address of the upper

left-hand corner where the first character will appear.  Upon return,

these registers are updated to give the address of the character to

the right, (or below if no more space exists on the line).  This

simplifies the composition of complex messages.

IX register contains the Alternate Font Descriptor.  It is required

only if alternate font is reference in call.  Each character must be

stored in one-bit per pixel format.

The small (3 X 5) character set is displayed using this facility.  A

word in the system DOPE vector points at a standard alternate font

descriptor for this character set.

The format of the alternate font descriptor is shown below.

+-----------------+

IX -> 0   | BASE CHARACTER  |   EQUAL TO FIRST CHARACTER IN TABLE

+-----------------+

1   | X FRAME SIZE    |   CHARACTER SIZE IN BITS + X SPACING

+-----------------+

2   | Y FRAME SIZE    |   CHARACTER SIZE IN BITS + Y SPACING

+-----------------+

3   | X PATTERN SIZE  |

+-----------------+   EACH CHARACTER TABLE ENTRY SHOULD BE OF

4   | Y PATTERN SIZE  |   SIZE X PATTERN*Y PATTERN SIZE

+-----------------+

5   | CHARACTER TABLE |

|     ADDRESS     |

6   |                 |

+-----------------+

SCREEN ALPHANUMERIC   DISNUM

DISPLAY BCD NUMBER

Calling Sequence:       SYSTEM  DISNUM

or

SYSSUK  DISNUM

DEFB    (X)

DEFB    (Y)

DEFB    (options)

DEFB    (extended options)

DEFW    (number address)

Arguments:              B  = Extended options

C  = Standard alphanumeric options byte

DE = Standard X,Y co-ordinate

HL = Address of BCD number

*NOT LOADED             IX = Optional character font descriptor

Outputs:                DE = Updated

Description:

This routine displays the standard BCD codes 0 through 9.  In addition,

the codes AH through FH are also defined.  The interpretation for

these codes are:        A = *     B = +     C = '

D = -     E = .     F = /

If leading zero suppress is set, then instead of displaying a leading

zero, a space is displayed.  The first non-zero nibble encountered

terminates leading zero suppression (including A - F).  If the number

is zero, a single zero is displayed.

If alternate font is set, the routine will display using codes between

AAH and B9H (zero starting at B0H).

SCREEN ALPHANUMERIC   DISTIM

DISPLAY TIME

Calling Sequence:       SYSTEM  DISTIM

or

SYSSUK  DISNUM

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (options)

Arguments:              DE = X,Y co-ordinates

X  = Options  (see note below)

IX = Alternate Font Descriptor  (not loaded)

Outputs:                DE = Updated

Description:

This routine displays the system time (GTMINS, GTSECS) at the co-

ordinates specified in the form MM:SS, where M=minutes, S=seconds.

Seconds are optional.

Notes:

The small character set is used and one level of enlarge factor

is permitted.

Options are the same as the alphanumeric display routine except

that bit 7=1 to display colon and seconds; bit 7=0 to suppress colon and

seconds.

SCREEN ALPHANUMERIC   CHRDIS

DISPLAY CHARACTER

Calling Sequence:       SYSTEM  CHRDIS

or

SYSSUK  CHRDIS

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (options)

DEFB    (Character)

Arguments:              A  = ASCII character to display

C  = Standard options byte

DE = Standard Y,X co-ordinates to begin at

*NOT LOADED             IX = Optional Alternate Font descriptor address

Outputs:                DE = Updated to next frame

Description:

This is the basic character display primitive.  If tabulation is

specified, the co-ordinates are updated but no actual writing occurs.

Notes:

Observe that IX is not loaded by the UPI SUCK facility.  If alternate

font is used, IX must be loaded with alternate descriptor address.

Since this routine uses magic memory, it is not re-entrant.

SCREEN ALPHANUMERIC   STRDIS

DISPLAY STRING

Calling Sequence:       SYSTEM  STRDIS

or

SYSSUK  STRDIS

DEFB    (X co-ordinate)

DEFB    (Y co-ordinate)

DEFB    (options)

DEFW    (String)

Arguments:              HL = String address

C  = Standard options byte

DE = Standard Co-ordinates

*NOT LOADED             IX = Alternate Font descriptor dddress

Outputs:                DE = Updated to next frame

Description:

The string pointed at by HL is displayed as optioned.  The string is

terminated by a zero byte.

Notes:

IX is not loaded by SUCK.  STRDIS is not re-entrant.

STRDIS INTERPRETATION OF CODES 64H to 7FH

-----------------------------------------

STRDIS responds to the character codes between 64H and 7FH, these codes

are taken to specify that certain registers in the context block are

to be set to new values.  This facility is useful for changing size,

write mode, screen co-ordinates, or fonts, during a single STRDIS call.

The following table specifies which registers are loaded for a given

code.  The order in which the new register data follows the code is

also represented.

64H        C               72H     IX,D

65H        E,C             73H     IX,E,D

66H        D,C             74H     IX,C

67H        E,D,C,          75H     IX,E,C

68H        NONE            76H     IX,D,C

69H        E               77H     IX,E,D,C

6AH        D               78H     IX

6BH        E,D             79H     IX,E

6CH        C               7AH     IX,D

6DH        E,C             7BH     IX,E,D

6EH        D,C             7CH     IX,C

6FH        E,D,C           7DH     IX,E,C

70H        IX              7EH     IX,D,C

71H        IX,E            7FH     IX,E,D,C

SCREEN VECTORING - VECTORING ROUTINES

-------------------------------------

Most games involve moving patterns.  Most moving patterns move along

a line.  The home video game operating system provides the vectoring

routines to facilitate programming such pattern motion.

The vectoring routines work with a memory array called a vector.

Represented within this vector are the co-ordinates of an object, the

velocities of the object, and the necessary status information to

control the object.  By periodically invoking the vectoring routine, this

data is updated and can be used to direct the motion of a pattern.

More formally, a vectored object possesses an X and Y co-ordinate.

Associated with these co-ordinates are velocities DELTA X and DELTA Y,

which are added to X and Y every time increment.  Since the screen is

finite, there also exists two upper and lower limits X_LU, X_LL, Y_LU,

and Y_LL, the attainment of which requires some response.

The HVGSYS vectoring routine allows for two different responses to a

limit attained.  Either the sign of the delta is reversed or vectoring

is stopped for this co-ordinate.  This is specified by a flag byte.

When attainment occurs, this fact is indicated by a status byte.  Also,

the co-ordinate is set equal to the limit that was attained, preventing

over-shoot.

Utilization of the vectoring routines involves a number of user

responsibilities.  The user must properly initialize certain fields in the

vector array.  He must increment the time base byte, and periodically

call the vectoring routine.  Status bits must be checked and writing must

be done.

To insure high-accuracy, co-ordinates and deltas are double- precision.

The assumed binary "decimal point" is between the high and low order byte.

The following diagrams explain the layout of the vector array and the

attendant user responsibilities.

VECTOR BLOCK

BYTE      FUNCTION        HVGLIB

NAME

+-------------------+--------+

0  |   MAGIC REGISTER  |  VBMR  | - DO NOT USE BIT 7

+-------------------+--------+

1  |   VECTOR STATUS   | VBSTAT |

+-------------------+--------+

2  |     TIME BASE     | VBTIMB |  - INCREMENTED BY USER

+-------------------+--------+

3  |                   | VBDXL  |

|      DELTA X      +--------+

4  |                   | VBDXH  |

+-------------------+--------+

5  |                   |  VBXL  |

|         X         +--------+

6  |                   |  VBXH  |

+-------------------+--------+

7  |   X CHECKS MASK   | VBXCHK |

+-------------------+--------+

8  |                   | VBDYL  |

|      DELTA Y      +--------+

9  |                   | VBDYH  |

+-------------------+--------+

10 |                   |  VBYL  |

|        Y          +--------+

11 |                   |  VBYH  |

+-------------------+--------+

12 |   Y CHECKS MASK   | VBYCHK |

+-------------------+--------+

13 |        OLD        | VBOAL  | - MAINTAINED BY USER

|      SCREEN       +--------+

14 |      ADDRESS      | VBOAH  |

+-------------------+--------+

VECTOR STATUS DETAIL

+--------+--------+--------+--------+--------+--------+--------+--------+

| Active | BLANK  |                         NOT                         |

| VBSACT | VBBLNK |                         USED                        |

+--------+--------+--------+--------+--------+--------+--------+--------+

ACTIVE                  Set by user to indicate that vector is active.  The

vectoring routines will do no processing if reset.

BLANK                   Must be initialized by user to reset state.  Thereafter

this bit is maintained by the VWRIT and VBLANK

system routines.

CHECKS MASK DETAIL

+--------+--------+--------+--------+--------+--------+--------+--------+

|                NOT                | LIMIT  |  NOT   |REVERSE | LIMIT  |

|                                   |ATTAINED|        | DELTA  | CHECK  |

|                USED               |        |  USED  | SIGN   |        |

|                                   | VBCLAT |        | VBCREV | VBCLMT |

+--------+--------+--------+--------+--------+--------+--------+--------+

LIMIT CHECK             Set by user to indicate that this co-ordinate is

to be limit checked.

REVERSE DELTA           Set by user to indicate that when this co-ordinate

attains it's limit, the sign of the associated delta

is to be reversed.  This can be used to cause objects

to 'bounce' off barriers.

LIMIT ATTAINED          Set by system if the limit was attained this call.

Otherwise it is reset.  If the delta was not changed,

either by Reverse Delta or user, this bit will stay set.

SCREEN VECTORING   VECT

VECTOR OBJECT IN TWO DIMENSIONS

Calling Sequence:       SYSTEM  VECT

or

SYSSUK  VECT

DEFW    (Vector address)

DEFW    (Limit table)

Arguments:              HL = Limit table address

IX = Vector address (points at VBMR)

Output:                 C  = Time base used

Z  = True, if it did not move

Description:

If the vector is inactive, control is returned immediately.  Otherwise

VECTC is called for X, then Y.  The zero status is determined by

comparing the new co-ordinate value with it's old value.  If the

high-order byte changed, then the object moved.  Zero status set if

object did not move, reset if object moved.

SCREEN VECTORING  VECTC

VECTOR A CO-ORDINATE

Calling Sequence:       SYSTEM  VECTC

or

SYSSUK  VECTC

DEFW    (co-ordinate address)

DEFW    (Limit table)

Arguments:              IX = Pointer to low-order byte of delta for co-ordinate

HL = Limits table for THIS CO-ORDINATE (if required)

C  = Time base to use

Description:

This routine operates on the subset of the vector array associated with

a single co-ordinate.  This subset consists of the delta co-ordinate

and checks mask.  This entry is provided so special vectoring schemes

may be implemented such as 1 dimensional or 3 dimensional vectoring.

This entry adds the delta to the co-ordinate time base times.  It then

performs the limit checks for the co-ordinate if optioned.

Note that this entry DOES NOT interrogate or alter any bytes in the

vector array outside of the defined subset.  Hence the active bit

isn't checked.

SCREEN   RELABS

CONVERT RELATIVE CO-ORDINATES TO ABSOLUTE MAGIC ADDRESS AND

SET UP MAGIC REGISTER

Calling Sequence:       SYSTEM  RELABS

or

SYSSUK  RELABS

DEFB    (Magic register value)

Arguments:              A  = Magic register value to set

D  = Y co-ordinate

E  = X co-ordinate

Output:                 A  = Magic register value, with proper shift amount set

DE = Absolute memory address (MAGIC)

Description:

The low-order two bits of the X co-ordinate are inserted into the magic

register value bitstring.  The absolute memory address corresponding to

the co-ordinate is computed, taking into consideration the value of the

flopped bit.  The co-ordinate systems used are shown below.

0           --->         159             159         <---           0

0 +----------------------------+           +----------------------------+

|                            |           |                            | 0

|                            |           |                            |

|                            |           |                            |

| |           NORMAL           |           |           FLOPPED          | |

| |        CO-ORDINATE         |           |         CO-ORDINATE        | |

V |           SYSTEM           |           |           SYSTEM           | V

|    (FLOPPED BIT RESET)     |           |      (FLOPPED BIT SET)     |

|                            |           |                            |

101 |                            |           |                            | 101

+----------------------------+           +----------------------------+

Proofing Note: 160/102 = 1.57 - Actual Screen Aspect Ratio

SCREEN   RELAB1

CONVERT RELATIVE ADDRESS TO ABSOLUTE NORMAL ADDRESS

Calling Sequence:       SYSTEM  RELAB1

or

SYSSUK  RELAB1

DEFB    (Magic register value)

Arguments:              A  = Magic register value to combine with shift amount

D  = Y co-ordinate

E  = X co-ordinate

Output:                 A  = Combined magic register value

DE = Absolute normal address (not magic)

Description:

This routine is identical to RELABS except that a non-magic address

is returned and the hardware magic register is not set.  The flopped

bit is interrogated and the flopped co-ordinate system is used,

if optioned.

SCREEN   COLSET

SET COLOR REGISTERS

Calling Sequence:       SYSTEM  COLSET

or

SYSSUK  COLSET

DEFW    (Address of color list)

Inputs:                 HL = Color list laid out

COL3L = first to

COLOR last  i.e.: COLOR would be at a higher

address than COL3L

Description:

This routine sets color registers and saves address of colors for

use by PIZBRK and BLAKOUT for color restoration.

[Proofing Note: BLAKOUT is seven letters (limit is six).  I can not find

anything close to this in the manual.  Thoughts?  Dec 16, 2001]

HUMAN   INCSCR

INCREMENT SCORE AND COMPARE TO END SCORE

Calling Sequence:       SYSTEM  INCSCR

or

SYSSUK  INCSCR

DEFW     (address of score)

Arguments:              HL = Address of score (must be 3 bytes long)

Output:                 Score incremented and optionally game over bit set

Description:

The 3 byte score pointed at by HL (BCD with low order byte at lowest

address) is incremented (by 1) and compared to the end score (ENDSCR).

If the end score bit (GSBSCR) was set in the game status byte (GAMSTB)

and end score has been reached, then the game over bit (GSBEND) is set

in the game status byte.

HUMAN   PAWS

PAUSE

Calling Sequence:       SYSTEM  PAWS

or

SYSSUK  PAWS

DEFB    (number of interrupts)

Arguments:              B  = Number of interrupts to wait

Description:

This routine provides for a pause for a certain number of interrupts.

If used with ACT INT, 60 will be a 1-second pause.  This routine

does an EI upon entry and assumes interrupts will occur.

HUMAN KEYBOARD   KCTASC

KEY CODE TO ASCII

Calling Sequence:       SYSTEM  KCTASC

Arguments:              B = Key code (Not loaded)

Output:                 A = ASCII equivalent of keycode

Description:            This routine does a table look-up

KEYCODE         NAME            GRAPHIC          HEX VALUE

-------         ----            -------          ---------

1               Clear           C                43

2               Up Arrow        *                5E

3               Down Arrow      *                5C

4               Percent         %                25

5               Recall          MR               52

6               Store           MS               53

7               Change Sign     CH               3B

8               Divide          *                2F

9               7               7                37

10              8               8                38

11              9               9                39

12              Times           X                2A

13              4               4                34

14              5               5                35

15              6               6                36

16              Minus           -                2D

17              1               1                31

18              2               2                32

19              3               3                33

20              Plus            +                2B

21              Clear Entry     CE               26

22              0               0                30

23              Decimal Point   .                2E

24              Equals          =                3D

* - Three names ('Up Arrow,' 'Down Arrow,' and 'Divide') do not have ASCII equivalent graphic marks.  An asterisk is NOT printed on screen.  Instead, the BPA uses three different non-ASCII symbols.  Each graphic looks as the name describes.

HUMAN CONTROLS & KEYPAD   SENTRY

SENSE TRANSITION

Calling Sequence:       SYSTEM  SENTRY

or

SYSSUK  SENTRY

DEFW    (Key mask address)

Arguments:              DE = Keypad mask table

Description:

SENTRY checks for changes in the potentiometers (pots), control

handles, triggers, keypad, semaphores and counter/timers.  It also

takes care of blackout.  Blackout is the automatic blacking-out of

the screen after 255 seconds without a change.  If SENTRY isn't called

then the game will not black out.

SENTRY checks if TIMOUT equals 0 on entry and if zero, it goes to

PIZBRK.  If a key has gone down or a control handle changed, then TIMOUT

is set to FFH.

HL should point at a keypad mask. The keypad consists of 6 rows

by 4 columns.

Example mask of         DEFB    011100B

just 0-9                DEFB    111100B

DEFB    011100B

DEFB    000000B

See diagram on following page.

+-------------+------------+------------+------------+

| 1           | 2          | 3          | 4          |

|      C      |     Up     |    Down    |      %     |  0

|             |    Arrow   |    Arrow   |            |

+-------------+------------+------------+------------+

| 5           | 6          | 7          | 8          |

|     MR      |     MS     |     CH     |  Division  |  1

|             |            |            |   Symbol   |

+-------------+------------+------------+------------+

| 9           | 10         | 11         | 12         |

|      7      |      8     |      9     |      X     |  2

|             |            |            |            |     MASK

+-------------+------------+------------+------------+     BIT

| 13          | 14         | 15         | 16         |     NUMBER

|      4      |      5     |      6     |      -     |  3

|             |            |            |            |

+-------------+------------+------------+------------+

| 17          | 18         | 19         | 20         |

|      1      |      2     |      3     |      +     |  4

|             |            |            |            |

+-------------+------------+------------+------------+

| 21          | 22         | 23         | 24         |

|     CE      |      0     |      .     |      =     |  5

|             |            |            |            |

+-------------+------------+------------+------------+

1             2            3            4

MASK BYTE NUMBER

+-------------+

KEY NUMBER ----- *           |

|      * ---------- FUNCTION

|             |

+-------------+

Output:               A = Return Code

B = Extended Code

PRIORITY        A=              MEANING

--------        --              -------

SNUL            Nothing Changed

1               SCT0            Counter/Timer 0 decremented by 0

to

1               SCT7            Counter/Timer 7 decremented to 0

2               SF0             SEMI4S bit 0 was 1

to

2               SF7             SEMI4S bit 7 was 1

4               SSEC            1 second has elapsed since the last SSEC

5               SKYU            Keypad went from down to up   B=0

5               SKYD            Key is down     B=key number

3               SP0             POT 0 changed   B=new value

to

3               SP3             Pot 3 changed   B=new value

6               SJ0             Joystick 0 changed    B=new value

to

6               SJ3             Joystick 3 changed    B=new value

6               ST0             Trigger 0 changed     B=new value

to

6               ST3             Trigger 3 changed    B = new value

Notes:

The potentiometers (pots) are debounced.  New trigger value=Trigger

off (0) or trigger on (10H).   When switches are actuated simultaneously

the order of return is: SCT7 TO SCT0, SF7 TO SF0, SP0 TO SP3, SSEC,

SKYU, SKYD, SJ0, ST0, SJ1, ST1, SJ2, ST2, SJ3, ST3.

HUMAN CONTROL   DOIT

RESPOND TO INPUT TRANSITION

Calling Sequence:       SYSTEM  DOIT

or

SYSSUK  DOIT

DEFW    (Do table)

Arguments:              A  = SENTRY return code

B  = Extended return code

HL = Do table address

Description:

The SENTRY return code is used to search the DOTABLE.  If the

transition is present in DOTABLE, then control is transferred to the

associated handling routine.  The handling routine may be MACRO or

machine instructions.  The routine receives registers as they are on

DOIT entry.  If no transition is found, execution continues at the

first instruction following call.  The DOTABLE is a linear list

composed of 3 byte entries, 1 entry per SENTRY return code.

+--------+--------+--------+--------+--------+--------+--------+--------+

|     TRANSFER    |                       RETURN                        |

|       TYPE      |                        CODE                         |

+--------+--------+--------+--------+--------+--------+--------+--------+

|                                                                       |

|                            HANDLER ADDRESS                            |

|                                                                       |

+-----------------------------------------------------------------------+

Where transfer type designates how handler address is to be transferred

to.  The codes are:  00=JMP to machine language routine and pop

context; 01=RCALL machine language routine in current context; 10=MCALL

interpreter routine in current context.  Mode 01 and 10 expect the

returned-to point to be interpretive, mode 0 expects it to be machine instructions.

End of list is indicated by a terminator byte which is greater than or

equal to C0H.

HUMAN CONTROL   PIZBRK

"COFFEE BREAK"  BLACK OUT SCREEN AND WAIT FOR KEY

Calling Sequence:       SYSTEM  PIZBRK

or

SYSSUK  PIZBRK

Input:                  None

Output:                 None

Description:

This routine blacks out the screen and waits for either a key press

or a trigger or a joystick change.

This function should be called whenever a "hold until further notice"

is needed.

All keys on the keypad are enabled.  Interrupts are disabled on

entry and enabled on exit.  It is a good idea to reset any 60th of a

second timers on exiting PIZBRK.

HUMAN CONTROLS   EXAMPLE

This routine echoes number keys and takes a coffee break on trigger

0 being pulled.  Assumes SP is set and screen erases.

SYSTEM  INTPC

LOOP:   DO      SENTRY

DEFW    NUMBAS

DO      DOIT

DEFW    DTAB

DO      MJUMP

DEFW    LOOP

NUMBAS: DEFB    011100B         ;NUMBER KEYS ONLY

DEFB    111100B

DEFB    011100B

DEFB    0

DTAB:   MC      SKYD,SHOW       ;IN KEY DOWN MACRO CALL

MC      ST0,PBREAK+END  ;ON TO MACRO CALL

SHOW:   DO      KCTASC          ;CONVERT TO ASCII

DO      SUCK

DEFB    00000111B       ;X,Y=0=DE

DEFB    11001100B       ;OPTIONS=C

DONT    CHRDIS          ;DISPLAY CHAR

MRET                    ;BACK TO LOOP

PBREAK: DO      PIZBRK          ;COFFEE BREAK

DO      MRET            ;BACK TO LOOP

INTERRUPT   MUSIC PROCESSOR

The music processor can be thought of as an independent CPU handling

all output to the music/noise ports.  The MUZCPU has 4 registers:

MPC:    Like all program counters, points to the next

data byte to fetch.

MSP:    Like a stack pointer, points to return

address in the stack.

Duration:    Is loaded at the start of a note and then

decremented every 60th of a second

Voice:    Is a status register.  It tells which voices

(tones) to load with what data.

The voices status register is shown below.  Execution proceeds

right-to-left.  Make sure that you always have at least one PC

incrementing bit or load on.

+--------+--------+--------+--------+--------+--------+--------+--------+

|   INC  |   OUT  |   INC  |   OUT  |   INC  |   OUT  |  OUT   |  OUT   |

|   PC   | TONE A |   PC   | TONE B |   PC   | TONE C | VIBRA  |  VOLN  |

+--------+--------+--------+--------+--------+--------+--------+--------+

MUZCPU INSTRUCTION SET

----------------------

# OF BYTES      MNEMONIC              COMMENT

----------      --------              -------

2           VOICES,(data)         ;VOICES=(data)

2           MASTER,(data)         ;TONE0=(data)

3           CALL,(address)        ;(SP)=(PC+3)  PC=address

1           RET                   ;PC=(SP++)

3           JP,(address)          ;PC=address

2           NOTE1                 ;Duration, note or data (D1)

3           NOTE2                 ;Duration, D1,D2

4           NOTE3                 ;Duration, D1,D2,D3

5           NOTE4                 ;Duration, D1,D2,D3,D4

6           NOTE5                 ;Duration, D1,D2,D3,D4,D5

2           REST                  ;Duration in 60ths of a second

;Pauses silently (except legato)

1           QUIET                 ;Stops music and sets volume=0

2           OUTPUT                ;Port #, Data

9           OUTPUT                ;SNDBX,DATA10,D11,D12,D13,D14,D15,D16,D17

3           VOLUME                ;(VOLAB),(VOLMC) sets volume for notes

1           PUSHN                 ;Push # between 1-16 onto the stack

1           CREL                  ;Call relative to next instruction

3           DSJNZ                 ;decrement stack top and jump

;if not 0, else pop stack

1           LEGSTA                ;flips between STACATO and LEGATO modes

;STACATO is clipped 1/60th before the

;end of each note

;LEGATO allows one note to run into

;the next

Note:           All durations are limited to a maximum of 127

MUSIC SCORE EXAMPLE

-------------------

VOICES  11010100B       ;ABC=DATA 1

MASTER  0A1H            ;ABC=1/2

VOLUME  88H,08H

NOTE1   12,A1

NOTE1   12,C2

NOTE1   24,E2

NOTE1   12,C2

NOTE1   12,E2

REST    6

VOICES  11110110B       ;Suck in Vibrato, AB and C bytes

NOTE3   12,14,A2,E2

QUIET

INTERRUPTS   MUSIC   BMUSIC

BEGIN PLAYING MUSIC

Calling Sequence:       SYSTEM  BMUSIC

or

SYSSUK  BMUSIC

DEFW    (Music stack)

DEFB    (voices byte)

DEFW    (Score)

Arguments:              A  = Voices to start with

HL = MUSIC PC (Score)

IX = Music SP

Description:

Quiets any previous music, then interprets "score".  See music

processor for more information.

INTERRUPTS   MUSIC   EMUSIC

STOP MUSIC

Calling Sequence:       SYSTEM  EMUSIC

or

SYSSUK  EMUSIC

Arguments:              NONE

Outputs:                NONE

Description:

Outputs 0 to volume ports and halts music processor.

INTERRUPTS   ACTINT

ACTIVE INTERUPTS

Calling Sequence:       SYSTEM  ACTINT

or

SYSSUK  ACTINT

Input:                  NONE

Output:                 NONE

Function:               Sets IM=2, INLIN=200, sets I reg + INFBK

Calls TIMEX and TIMEY

Enables interrupts

Description:

Once ACTINT is called, it provides interrupt service completely

automatically.  It runs the seconds timer, the game timer, the music

processor, and black-out timers, plus CT0, CT1, CT2, CT3.  Functions

as 60th of a second timers.

INTERRUPTS   TIMERS   DECCTS

DECREMENT COUNTER/TIMERS

Calling Sequence:       SYSTEM  DECCTS

or

SYSSUK  DECCTS

DEFB    (Mask)

Input:                  C  = Mask indicative which counters to decrement.

Output:                 Sentry will notify the program.

Description:

Decrements counter if they are non-zero.  If any go from 1 to 0,

sentry is notified.

INTERRUPTS   TIMERS   CTIMER

Calling Sequence:       CALL    CTIMER

Input:                  HL = Address of custom time base

B  = Value to load into time base 1 to 0 transition

C  = CT mask as in DECCTS

Description:

HL is loaded and decremented.  If it is not = 0, then a return is

executed.  Else, HL is loaded with B and DECCTS is called.

Registers HL, DE, BC, and AF are undefined upon exit.

INTERRUPTS   TIMERS   STIMER

DECREMENT TIMERS

Calling Sequence:       PUSH    AF

PUSH    BC

PUSH    DE

PUSH    HL

CALL    STIMER

POP     HL

POP     DE

POP     BC

POP     AF

Input:                  NONE

Description:            STIMER keeps track of game time.  If it hits 0,

then the GSBEND bit in the game status byte is set.

Uses:                   AF, BC, DE, HL

Calls:                  Music processor on note (duration) expiration.

Note:                   Sets bit 7 of key sex to 1 on every second.

MOVE   MOVE BYTES

Calling Sequence:       SYSTEM  MOVE

or

SYSSUK  MOVE

DEFW    (Destination)

DEFW    (Number of bytes)

DEFW    (Source)

Arguments:              DE = Destination address

HL = Source address

BC = Number of bytes to transfer

Description:            MOVE uses LDIR to copy bytes from source

to destination.

INDEXN   INDEX NIBBLE

Calling Sequence:       SYSTEM  INDEXN

or

SYSSUK  INDEXN

DEFW    (Base Address)

Arguments:              C  = Nibble displacement (0 - 255)

HL = Base address of table

Output:                 A  = Nibble value

Description:

INDEXN is used to look up a given nibble in a liner list.

The indexing works like:

+-------+-------+

BASE ADDRESS  |   1   |   0   |

+-------+-------+

1  |   3   |   2   |

+-------+-------+

2  |   5   |   4   |

+-------+-------+

3  |   7   |   6   |

+-------+-------+

.  |       |       |

.  |       |       |

STOREN   STORE NIBBLE

Calling Sequence:       SYSTEM  STOREN

or

SYSSUK  STOREN

DEFW    (Base address)

Arguments:              C  = Nibble displacement        *NOT LOADED

HL = Base address

A  = Nibble value to store      *NOT LOADED

Description:            STOREN is the inverse of INDEXN.

STOREN works as with INDEXN.

INDEXW   INDEX WORD

Calling Sequence:       SYSTEM  INDEXW

or

SYSSUK  INDEXW

DEFW    (Base address)

Arguments:              A  = Displacement (0 - 255)     *NOT LOADED

HL = Base address of table

Output:                 DE = Entry looked up

HL = Address of entry looked up

Description:            Indexing looks like:

DISPLACEMENT

+---------------+

BASE ADDRESS  |               |       0

+---------------+

1  |               |

+---------------+

2  |               |       1

+---------------+

3  |               |

+---------------+

4  |               |       2

+---------------+

5  |               |

+---------------+

.  |               |       .

.  |               |

INDEXB   INDEX BYTE

Calling Sequence:       SYSTEM  INDEXB

or

SYSSUK  INDEXB

DEFW    (Base Address)

Arguments:              A  = Displacement (0 - 255)

HL = Base address of table

Output:                 A  = Entry looked up

HL = Address of entry looked up

Notes:

INDEXB returns the byte at address

(Base address) + (Displacement)

SETB   STORE BYTE

Calling Sequence:       SYSTEM  SETB

or

SYSSUK  SETB

DEFB    (Value to store)

DEFW    (Address)

Arguments:              A  = Byte value to store

HL = Address to be set

Description:            Stores an 8-bit value at a specified address.

SETW   STORE WORD

Calling Sequence:       SYSTEM  SETW

or

SYSSUK  SETW

DEFW    (Value to store)

DEFW    (Address)

Arguments:              DE = Word value to store

HL = Address to be set

Description:           Stores a 16-bit value at a specified address.

CARTRIDGE CONVENTIONS

---------------------

Two types of cartridges may be used with the Bally Professional Arcade.

The first type, called an autostart cartridge, is entered immediately

after reset.  The only initialization that is performed before entry

is the set-up of the stack pointer to point just below system RAM and

the establishment of "consumer mode" in the custom chips.  RAM is not

altered in this mode.

The second type, called a standard cartridge, is entered after a game

selection process is completed.  Considerably more initialization is

done by the system before control transfer.

1)      System RAM is cleared to 0

2)      The ACTINT interrupt routine is enabled

3)      The MENU colors are set in the left color map

4)      Vertical blank is set at line 96, horizontal

boundary at 41, and interrupt mode at 8.

5)      The screen displays the menu frame.

6)      The shifter is cleared.

An autostart cartridge is indicated by a jump instruction (opcode C3H)

at location 2000H.  This jump instruction should branch to the starting

address of the cartridge.

A standard cartridge is indicated by a sentinel byte of 55H at location

2000H.  Following this byte is the first node of the cartridge's menu

data structure.  This data structure gives the name and starting

address of each program in the cartridge.  (See MENU)

When the user has selected a cartridge game, control is transferred

to the starting address with the address of the program name string

in the registers.  The cartridge program will use the GETPAR system

routine to prompt for game parameters such as score to play to,

game time limit or number of layers.

The cartridge has access to the six unused restart instructions.   See

the following cartridge diagram for the transfer vectors.

BYTE

+-----+-----+-----+-----+-----+-----+-----+-----+

2000  |  0  |  1  |  0  |  1  |  0  |  1  |  0  |  1  |  SENTINEL ($55)

+-----+-----+-----+-----+-----+-----+-----+-----+  \

1  |                                               |  |

2  |                 NEXT MENU NODE                |  |

+-----------------------------------------------+  |  MENU NODE FOR

3  |                                               |   > FIRST GAME ON

4  |         STRING ADDRESS FOR FIRST GAME         |  |  CARTRIDGE

+-----------------------------------------------+  |

5  |                                               |  |

6  |         START ADDRESS FOR FIRST GAME          |  |

+-----------------------------------------------+  /

7  |                                               |  \

8  |                     RST 8                     |  |

9  |                  JUMP VECTOR                  |  |

+-----------------------------------------------+  |

A  |                                               |  |

B  |                     RST 16                    |  |

C  |                                               |  |

+-----------------------------------------------+  |

D  |                                               |  |

E  |                     RST 24                    |  |

F  |                                               |  |

+-----------------------------------------------+  |  THESE CELLS

2010  |                                               |  |  MAY BE USED

1  |                     RST 32                    |  |  FOR PROGRAM

2  |                                               |   > IF THE

+-----------------------------------------------+  |  ASSOCIATED

3  |                                               |  |  RST OR HOOK

4  |                     RST 40                    |  |  IS NOT USED

5  |                                               |  |

+-----------------------------------------------+  |

6  |                                               |  |

7  |                     RST 48                    |  |

8  |                                               |  |

+-----------------------------------------------+  |

9  |                                               |  |

A  |          SENTRY HOOK TRANSFER VECTOR          |  |

B  |             USED FOR DEMO PROGROMS            |  |

+-----------------------------------------------+  /

HUMAN   GETPAR

GET GAME PARAMETER

Calling Sequence:       SYSTEM  GETPAR

or

SYSSUK  GETPAR

DEFW    (Prompt)

DEFB    (Digits)

DEFW    (Parameter)

Arguments:              A  = Number of digits to get

BC = Address of prompt string

DE = Title string address        *NOT LOADED

HL = Address of parameter to get

Description:

A menu frame is created displaying the title passed in DE at the top.

The message "ENTER" is displayed in the center of the screen followed

by the prompt string.  GETNUM is entered with feedback specified

in 2X enlarged characters.  After entry is complete, GETPAR pauses

for 1/4 second to allow user to see his entry and then returns.

Notes:

See entry conditions and resource requirements for menu.

Prompt string example: "# OF PLAYERS"

The title string address (DE) is usually the title returned from MENU.

The address of parameter to get (HL), HL points at the low-order byte

of BCD number in RAM.

HUMAN   MENU

DISPLAY MENU AND BRANCH ON SELECTION

Calling Sequence:       SYSTEM  MENU

or

SYSSUK  MENU

DEFW    (Title)

DEFW    (List)

Arguments:              DE = Address of menu title string

HL = Address of menu list

Output:                 DE = String address of selection mode

Description:

The title is displayed at the top of the screen.  Each entry in the

menu list is then displayed with a preceding number supplied by MENU.

GETNUM is called to get the selection number.  The menu list is searched

for the selected node and it is jumped to.

Notes:

A maximum of eight entries may appear.

On entry, MENU expects interrupts to be enabled, colors and boundaries

to be set up.  MENU uses 96 lines of screen, creams the alternate set,

and requires three levels of context.  MENU calls SENTRY and thus 'eats'

all irrelevant transitions.

+----------+

|   NEXT   |    ADDRESS OF NEXT NODE ON LIST

|          |    ZERO IF THIS NODE IS LAST

+----------+

|   STRING |    ADDRESS OF NAME OF THIS SELECTION

|          |    THIS IS WHAT IS PASSED IN DE

+----------+

|   GO TO  |    WHERE TO BRANCH TO IF THIS

|          |    SELECTION IS SELECTED

+----------+

Proofing Note: 'creams the alternate set' = 'creates the alternate set?'

HUMAN   GETNUM

GET NUMBER

Calling Sequence:       SYSTEM  GETNUM

or

SYSSUK  GETNUM

DEFB    (X address)

DEFB    (Y address)

DEFB    (CHRDIS options)

DEFB    (DISNUM options)

DEFW    (Number address)

Arguments:              B  = Display number routine options

C  = Character display routine options

DE = Y,X co-ordinate for feedback

HL = Address of where to put entered number

Description:

This routine inputs a number from either the keypad or the pot on

control handle of player one.  Keypad entry has priority.  The routine

exits when the specified number of digits were entered or = is pressed

on the keypad.

Pot entry is enabled by pressing the trigger.  The current pot value is

then shown.  Twist the pot until the number you want is shown.  Then

press the trigger again to complete the entry.  The pot can only enter 1

or 2 digits.  If a group of numbers is being entered, the user must

enable entry for each new number.

DISPLAY NUMBER OPTIONS

+------+------+------+------+------+------+------+------+

| ZERO |  ALT |    NUMBER OF DIGITS TO DISPLAY/ACCEPT   |

| SUPP | FONT |      |      |      |      |      |      |

+------+------+------+------+------+------+------+------+

CHARACTER DISPLAY OPTIONS

+------+------+------+------+------+------+------+------+

|   ENLARGE   | XOR  |   OR |      ON     |     OFF     |

|   FACTOR    |      |      |    COLOR    |    COLOR    |

+------+------+------+------+------+------+------+------+

HUMAN   MSKTD

JOYSTICK MASK TO DELTAS

Calling Sequence:       SYSTEM  MSKTD

or

SYSSUK  MSKTD

DEFW    (X Delta)

DEFB    (Flop flag)

DEFW    (Y Delta)

Arguments:              B  = Joystick mask       *NOT LOADED

C  = Flop flag

DE = X positive delta

HL = Y positive delta

Output:                 DE = X Delta

HL = Y Delta

Description:

This routine uses the joystick mask and flop flag to conditionally

modify the passed deltas.  If negative direction is indicated, the delta

is 2's complemented: if no direction is indicated, 0 is returned.

Note:                   B is not sucked [by SYSSUK].

MATH   RANGED

RANGED RANDOM NUMBER

Calling Sequence:       SYSTEM  RANGED

or

SYSSUK  RANGED

DEFB    (N)

Arguments:              A = N where 0 is less than or equal to a random

number less than N

(ie: for a random number of 0,1,or 2, N=3)

Output:                 A = Random Number

Notes:

If N is a power of 2, it is considerably faster to use N=0 which causes

an 8-bit value to be returned without ranging.  Use an AND instruction

to range it yourself.

This routine uses a polynomial shift register RANSHT in system RAM.

RANGED is called in GETNUM while waiting for game selection/parameter

entry.  Thus each execution of a program will receive different random

numbers.  For 'predictable' random numbers, alter RANSHT yourself after

parameter acceptance.

Introduction

------------

The Bally Professional Arcade is a full-color video game system based

on the mass-ram-buffer technique.  A mass-ram-buffer system is one in

which one or more bits of RAM are used to define the color and

intensity of a pixel on the screen.  The picture on the screen is

defined by the contents of RAM and can easily be changed by modifying RAM.

The system uses a Z-80 Microprocessor as it's main control unit.  The

system ROM has software for four games:  Gunfight, Checkmate,

Scribbling, and Calculator.  Additional ROM can be accessed through

the cartridge connector.  Three custom chips are used

for the video interface, special video processing functions, keyboard

and control handle interface, and audio generation.

The system exists in both high-resolution and low-resolution models.

The three custom chips can operate in either mode.  The mode of operation

is determined by bit 0 of output port 8H.  It must be set to 0

for low-resolution and 1 for high-resolution.  This bit is not set

to 0 at power up and must be set by software before any RAM operations

can be performed.

Memory Map

----------

In both the low and high resolution models, the operating system

ROM is in the first 8K of memory space.  The cartridge ROM

is in the space from 8K to 16K.  The standard screen RAM begins

at 16K.  In the low-resolution unit, standard screen RAM is 4K

bytes; in the high-resolution unit it is 16K bytes.  Magic screen RAM

begins at location 0.  It is the same size as standard screen RAM.  All

memory above 32K is available for expansion.  In the low-resolution

unit, memory space 20K - 32K is available for expansion.

When data is read from a memory location between 0 and 16K the data

comes from the ROM.  When data is written in a memory location (X)

between 0 and 16K, the system actually writes a modified form of the

data in location X+16K.  The modification is performed by the magic

system in the Data Chip and Address Chip.  Thus the RAM from 0 to 16K

is called Magic Memory.

Memory Map - Low-Resolution

---------------------------

Memory Map - High-Resolution

----------------------------

Screen Map

----------

In the Bally Professional Arcade, two bits of RAM are used to define

a pixel on the screen.  One 8-bit byte of RAM therefor defines four

pixels on the screen.

In the low-resolution model there are 40-bytes used to define a line

of data.  This gives a horizontal resolution of 160 pixels.  The

vertical resolution is 102 lines.  The screen therefor requires

102 X 40 = 4,080 bytes.  The remaining 16 bytes of the 4K RAM are used

for scratch pad.  More of the RAM may be used for scratchpad by blanking

the screen before the 102nd line.  This will be described later.

In the High-resolution model there are 80 bytes and 320 pixels per line.

The 204 lines require 16,320 bytes of RAM.  64 bytes of the 16K RAM are

left for scratch pad.

In both models the first byte of RAM is in the upper left-hand corner

of the screen.  As the RAM address increases, the position on the screen

moves in the same directions as the TV scan; from left-to-right and

from top-to-bottom.  The four pixels in each byte are displayed with

the least significant pixel, the one defined by bits 0 and 1, on

the right.

Screen Map - Low Resolution

---------------------------

Screen Map - High Resolution

----------------------------

Color Mapping

-------------

Two bits are used to represent each pixel on the screen.  These two

bits, along with the LEFT/RIGHT bit which is set by crossing the

horizontal color boundary, map each pixel to one of eight different color

registers.  The value in the color register then defines the color and

intensity of the pixel on the screen.  The intensity of the pixel is

defined by the three least significant bits of the register, 000 for

darkest and 111 for lightest.  The color is defined by the five most

significant bits.  The color registers are at output ports 0 through 7;

register 0 at port 0, register 1 at port 1, etc.

The color registers can be accessed as individual ports or all eight

can be accessed by the OTIR instruction.  The OTIR instruction is to

port BH (register C=BH) and register B should be set to 8.  The eight

bytes of data pointed to by HL will go to the color registers.

HL --> Memory Location X   Color Register 7

X+1 Color Register 6

X+2 Color Register 5

X+3 Color Register 4

X+4 Color Register 3

X+5 Color Register 2

X+6 Color Register 1

X+7 Color Register 0

The horizontal color boundary (bits 0-5 of port 9) defines the horizontal position of an imaginary vertical line on the screen.  The boundary

line can be positioned between any two adjacent bytes in the low-

resolution system.  The line is immediately to the left of the byte

whose number is sent to bits 0-5 of port 9.  For example, if the horizontal color boundary is set to 0, the line will be just to the left of

byte 0; if it is set to 20, the line will be between bytes 19 and 20 in

the center of the screen.

If a pixel is to the left of the boundary, its LEFT/RIGHT bit is set

to 1.  The LEFT/RIGHT bit is set to 0 for pixels to the right of the

boundary.  Color registers 0-3 are used for pixels to the right of the

boundary and registers 4-7 are used for pixels to the left of the

boundary.

In the high-resolution system, the boundary is placed in the same

position on the screen but between different bytes.  If the value X

is sent to the horizontal color boundary, then the boundary will be

between bytes 2X and 2X-1.  If the value 20 is sent, the boundary will

be between 39 and 40, in the center of the screen.

To put the entire screen, including the right side background, on

the left side of the boundary, set the horizontal color boundary to 44.

BACKGROUND COLOR

----------------

On most televisions the area defined by RAM is slightly smaller than the

screen.  There is generally extra space on all four sides of the RAM

area.  The color and intensity of this area is defined by the background

color number (bits 6 and 7 of port 9).  These two bits, along with

the LEFT/RIGHT bit point to one of the color registers which determines

the color and intensity.

VERTICAL BLANK

--------------

The Vertical Blank Register (output port AH) contains the line number

on which vertical blanking will begin.  In the low-resolution system

bit 0 should be set to 0 and the line number should be in bits 1-7.

In the high-resolution system the line number is in bits 0-7.  The

background color will be displayed from the vertical blank line to the

bottom of the screen.  This allows the RAM that would normally be

displayed in that area to be used for scratch pad.  If the vertical

blank register is set to 0 the entire RAM can be used for scratch pad.

In a low-resolution system the register must be set to 101 or less;

in a high-resolution system it must be set to 203 or less.

SUMMARY

-------

The following color register map shows which color registers are used

to define colors in different areas of the screen.  The map assumes the

background color is set to 0.  If it were set to 1 then color registers

1 and 5 would be used for background instead of 0 and 4.  In the low-

resolution system the color boundary is between bytes X and X-1.  In

the high-resolution system the boundary is between bytes 2X and 2X-1.

COLOR REGISTER MAP

------------------

INTERRUPT FEEDBACK

------------------

When the Z-80 acknowledges an interrupt it reads 8 bits of data from

the data bus.  It then uses this data as an instruction or an address.

In the Bally Professional Arcade this data is determined by the contents

of the interrupt feedback register (output port DH).  In responding

to a screen interrupt the contents of the interrupt feedback register

are placed directly on the data bus.  In responding to a light pen

interrupt the lower four bits of the data bus are set to 0 and the upper

four bits are the same as the corresponding bits of the feedback register.

INTERRUPT CONTROL BITS

----------------------

In order for the Z-80 to be interrupted the internal interrupt enable

flip-flop must be set by an EI instruction and one or two of the external

interrupt enable bits must be set (output port EH).  If bit 1 is set,

light pen interrupts can occur.  If bit 3 is set, screen interrupts can

occur.  If both bits are set, both interrupts can occur and the screen

interrupt has higher priority.

The interrupt mode bits determine what happens if an interrupt occurs

when the Z-80's interrupt enable flip-flop is not set.  Each of the two

interrupts may have a different mode.  In mode 0 the Z-80 will continue

to be interrupted until it finally enables interrupts and acknowledges

the interrupt.  In mode 1 the interrupt will be discarded if it is not

acknowledged by the next instruction after it occurred.  If mode 1 is used

the software must be designed such that the system will not be executing

certain Z-80 instructions when the interrupt occurs.  The opcodes of

these instructions begin with CBH, DDH, EDH, and FDH.

The mode bit for the light pen interrupt is bit 0 of port EH and the mode

bit for screen interrupt is bit 2 of EH.

SCREEN INTERRUPT

----------------

The purpose of the screen interrupt is to synchronize the software

with the video system.  The software must send a line number to the

interrupt line register (output port FH).  In the low-resolution system

bit 0 is set to 0 and the line number is sent to bits 1-7.  In the high-

resolution system the line number is sent to bits 0-7.  If the screen

interrupt enable bit is set, the Z-80 will be interrupted when the video

system completes scanning the line in the interrupt register.  This

interrupt can be used for timing since each line is scanned 60 times

a second.  It can also be used in conjunction with the color registers

to make as many as 256 color-intensity combinations appear on the screen

at the same time.

LIGHT PEN INTERRUPT

-------------------

The light pen interrupt occurs when the light pen trigger is pressed

and the video scan crosses the point on the screen where the light pen

is.  The interrupt routine can read two registers to determine the

position of the light pen.  The line number is read from the vertical

feedback register (input port EH).  In the high-resolution system the

line number is in bits 0-7.  In the low resolution system the line number

is in bits 1-7, bit 0 should be ignored.  The horizontal position of the

light pen can be determined by reading input port FH and subtracting 8.

In the low resolution system the resultant value is the pixel number,

0 to 159.  In the high-resolution system the resultant must be multiplied

by two to give the pixel number, 0 to 358.

MAGIC REGISTER

--------------

As described earlier, the Magic System is enabled when data is written

to a memory location (X) from 0 to 16K.  A modified form of the data is

actually written in memory location X+16K.  The magic register (output

port CH) determines how the data is modified.  The purpose of each bit

of the magic register is shown below.

Bit 0     LSB of shift amount

1     MSB of shift amount

2     Rotate

3     Expand

4     OR

5     XOR

6     Flop

The order in which magic functions are performed is as follows:

Expansion is done first; rotating or shifting; flopping; OR or XOR.

As many as four can be used at any one time and any function can be

bypassed.  Rotate and shift as well as OR and XOR cannot be done at

the same time.

EXPAND

------

The expander is used to expand the 8 bit data bus into 8 pixels (or

16 bits).  It expands a 0 on the data bus into a two-bit pixel and a

1 into another two-bit pixel.  Thus, two-color patterns can be stored

in ROM in half the normal memory space.

During each memory write instruction using the expander, either the

upper half or the lower half of the data bus is expanded.  The half

used is determined by the expand flip-flop.  The flip-flop is reset by

an output to the magic register and is toggled after each magic memory

write.  The upper half of the data bus is expanded when the flip-flop

is 0, and the lower half when the flip-flop is 1.

The expand register (output port 19H) determines the pixel values

into which the data bus will be expanded.  A 0 on the data bus will be

expanded into the pixel defined by bits 0 and 1 of the expand register.

A 1 on the data bus will be expanded into the pixel defined by bits

2 and 3 of the expand register.

The pixels generated by bit 0 or 4 of the data bus will be the least

significant pixel of the expanded byte.  The most significant pixel

will come from bit 3 or 7.

SHIFTER

-------

The shifter, flopper, and rotater operate on pixels rather than bits.

Each byte is thought of as containing four pixels, each of which has

one of four values.  The four pixels are referred to as P0, P1, P2,

and P3.  P0 is composed of the first two bits of the byte.

The shifter shifts data 0, 1, 2, or 3 pixels to the right.  The shift

amount is determined by bits 0 and 1 of the magic register.  The pixels

that are shifted out of one byte are shifted into the next byte.  Zero's

are shifted into the first byte of a sequence.  The shifter assumes the

first byte of a sequence is the first magic memory write after an output

to the magic register.  Each sequence must be initialized by an output

to the magic register and data cannot be sent to the magic register in

the middle of a sequence.

FLOPPER

-------

The output of the flopper is a mirror image of it's input.  Pixel 0

and 3 exchange values as do pixel 1 and 2.

The diagrams on the following page show examples of shifting

and flopping.

SHIFTER - FLOPPER

-----------------

ROTATOR

-------

The rotater is used to rotate a 4 X 4 pixel image 90 degrees in a clock-

wise direction.  The rotator is initialized by an output to the magic

register and will re-initialize itself after every eight writes to

magic memory.  To perform a rotation, the following procedure must be

performed twice.  Write the top byte of the unrotated image to a location

in magic memory.  Write the next byte to the first location plus 80, the

next byte to the first location plus 160, and the last byte to the first

location plus 240.  After eight writes the data will appear in RAM and

on the screen rotated 90 degrees from the original image.

The rotator can only be used in commercial mode.

The diagram on the following page shows an example of rotating.

ROTATOR

-------

OR AND XOR

----------

These functions operate on a byte as 8-bits rather than four pixels.

When the OR function is used in writing data to RAM, the input to the

OR circuit is ORed with the contents of the RAM location being accessed.

The resultant is then written in RAM.

The XOR function operates in the same way except that the data is

XORed instead of ORed.

INTERCEPT

---------

Software reads the intercept register (input port 8H) to determine if

an intercept occurred on an OR or XOR write.  An intercept is defined as the

writing of a non-zero pixel in a pixel location that previously contained

a non-zero pixel.  A non-zero pixel is a pixel with a value of 01, 10, or 11.

A 1 in the intercept register means an intercept has occurred.  Bits 0 - 3

give the intercept information for all OR or XOR writes since the last

input from the intercept register.  An input from the intercept register

resets these bits.  A bit is set to 1 if an intercept occurs in the

appropriate position and will not be reset until after the next intercept

register input.

Bit

0  Intercept in pixel 3 in an OR or XOR write since last reset

1  Intercept in pixel 2 in an OR or XOR write since last reset

2  Intercept in pixel 1 in an OR or XOR write since last reset

3  Intercept in pixel 0 in an OR or XOR write since last reset

4  Intercept in pixel 3 in last OR or XOR write

5  Intercept in pixel 2 in last OR or XOR write

6  Intercept in pixel 1 in last OR or XOR write

7  Intercept in pixel 0 in last OR or XOR write

PLAYER INPUT

------------

The system will accommodate up to four player control handles at once.

Each handle has five switches and a potentiometer.  The switches are

read by the Z-80 on input ports 10H - 13H and are not debounced.

The switches are normally open and normally feedback 0's.

The signals from the potentiometers are changed to digital information

by an 8-bit Analog-to-Digital Converter.  The four pots are on input ports

1CH - 1FH.  All 0's are fedback when the pot is turned fully counter-

clockwise and all 1's when turned fully clockwise.

The 24-button keypad is read on bits 0-5 of ports 14H-17H.  The data

is normally 0 and if more than one button is depressed, the data should

be ignored.  The keypad will not send back the proper data if any of

the player control switches are closed.  Here again, the buttons are

not debounced.

Player control inputs are shown on the following page.

PLAYER INPUT

------------

MASTER OSCILLATOR

-----------------

The frequency of the master oscillator is determined by the contents

of several output ports.  Port 10H sets the master frequency.  It is

given by the following formula:

1789

F_m = ------------ Khz

PORT 10H + 1

If bit 4 of output port 15H is set to 1, the master oscillator

frequency will be modulated by noise.  The amount of modulation will be

set by the 8-bit noise volume register, output port 17H.

If bit 4 of output port 15H is set to 0, the frequency of the master

oscillator will be modulated by a constant value to give a vibrato

effect.  The amount of modulation will be set by the vibrato depth

register (the first 6 bits of output port 14H).  The speed of the modulation

is set by the vibrato speed register (upper 2 bits of output port 14H);

00 for fastest and 11 for slowest.

Frequency modulation is accomplished by adding a modulation value to the

contents of port 10H and sending the result to the master oscillator

frequency generator.  In noise modulation, the modulation value is an

8-bit word from the noise generator.  If a bit in the noise volume

register is set to 0, the corresponding bit in the modulation value

word will be set to 0.  In vibrato modulation, the modulation value

alternates between 0 and the contents of the vibrato volume register.

Modulation can be completely disabled by setting the master volume to 0

if noise modulation is being used, or by setting the vibrato depth

to 0 when vibrato is used.

TONES

-----

The system contains three tone generators each clocked by the same

master oscillator.  The frequency of Tone A is set by output port 11H,

Tone B by output port 12H, and Tone C by output port 13H.  The

frequency is given by the following formula:

F_m                                  894

F_. = -----------------------------  =  ----------------------------------- Khz

2(contents of TONE PORT + 1)     (PORT 10H+1) (contents of TONE PORT+1)

Proofing Note: 'F_.' = 'F Subscript Up-Arrow'

The tone volumes are controlled by the output ports 15H and 16H.  The

lower 4 bits of port 16H set Tone A Volume, the upper 4 bits set Tone

B Volume.  The lower 4 bits of port 15H set Tone C Volume.  Noise can

be mixed with the tones by setting bit 5 of port 15H to 1.  In this case

the noise volume is given by the upper 4 bits of port 17H.  In all

cases a volume of 0 is silence and a volume of all 1's is loudest.

SOUND BLOCK TRANSFER

--------------------

All 8 bytes of sound control can be sent to the audio circuit with

one OTIR instruction.  Register C should be sent to 18H, register

B to 8H, and HL pointing to the 8 bytes of data.  The data pointed to

by HL goes to port 17H and the next 7 bytes of data goes to ports 16H

through 10H.

HL ->   Memory Location  X    Data-to-port  17H

X+1  Data-to-port  16H

X+2  Data-to-port  15H

X+3  Data-to-port  14H

X+4  Data-to-port  13H

X+5  Data-to-port  12H

X+6  Data-to-port  11H

X+7  Data-to-port  10H

AUDIO GENERATOR BLOCK DIAGRAM

-----------------------------

OUTPUT PORTS

------------

PORT NUMBER    FUNCTION

-----------    --------

0H         Color Register 0

1H         Color Register 1

2H         Color Register 2

3H         Color Register 3

4H         Color Register 4

5H         Color Register 5

6H         Color Register 6

7H         Color Register 7

8H         Low/High Resolution

9H         Horizontal Color Boundary, Background Color

AH         Vertical Blank Register

BH         Color Block Transfer

CH         Magic Register

DH         Interrupt Feedback Register

EH         Interrupt Enable and Mode

FH         Interrupt Line

10H         Master Oscillator

11H         Tone A Frequency

12H         Tone B Frequency

13H         Tone C Frequency

14H         Vibrato Register

15H         Tone C Volume, Noise Modulation Control

16H         Tone A Volume, Tone B Volume

17H         Noise Volume Register

18H         Sound Block Transfer

19H         Expand Register

INPUT PORTS

-----------

PORT NUMBER    FUNCTION

-----------    --------

8H         Intercept Feedback

EH         Vertical Line Feedback

FH         Horizontal Address Feedback

10H         Player 1 Handle

11H         Player 2 Handle

12H         Player 3 Handle

13H         Player 4 Handle

14H         Keypad Column 0 (right)

15H         Keypad Column 1

16H         Keypad Column 2

17H         Keypad Column 3 (left)

SYSTEM BLOCK DIAGRAM

--------------------

MICROCYCLER

-----------

The purpose of the microcycler is to combine the 16-bit Address Bus

and the 8-bit Data Bus from the Z-80 into one 8-bit Microcycle Data Bus

to the Data Chip, Address Chip, and I/O Chip.  This was done to reduce

the pin count on the custom chips.

The Microcycle Data Bus can be in any of four modes.  Its mode is

controlled by MC0 and MC1 coming from the Data Chip and RFSH# from the

Z-80.  The modes are shown below.

RFSH#         MC0    MC1         Microcycle Data Bus Contents

-----         ---    ---         ----------------------------

0            0      0          A0 - A7 from Z-80

0            0      1          A0 - A7 from Z-80

0            1      0          A0 - A7 from Z-80

0            1      1          A0 - A7 from Z-80

1            0      0          A0 - A7 from Z-80

1            0      1          A8 - A15 from Z-80

1            1      0          D0 - D7 from Z-80

1            1      1          D0 - D7 to Z-80

MC0 and MC1 change 140 usec after the rising edge of Phi.  Their

changes are shown in the timing diagrams of various instruction cycles.

MICROCYCLER BLOCK DIAGRAM

-------------------------

ADDRESS CHIP DESCRIPTION

------------------------

The Microcycle Decoder generates twelve bits of Z-80 address from the

8-bit Microcycle Data Bus.  This address is then fed through MUX I and

MUX II to MA0-5 which go to the RAM.  The Scan Address Generator

generates a 12-bit address which is used to read video data from the

RAM.  This address goes from 0 to FFFH once every frame (1/60 sec.).

MUX I sends either the Scan Address or Z-80 Address to its 12 outputs.

An output of the Scan Address Generator controls MUX I.  If the Scan

Address Generator and the Z-80 request memory cycle at the same time,

the Scan Address Generator will have higher priority and the Z-80 will

be required to wait (by the WAIT# output).  The Scan Address Generator

never requires the memory for more than one consecutive memory cycle,

so the Z-80 is never required to wait for the memory for more than one

cycle.  HORIZ DR and VERT DR synchronize the Scan Address Generator

with the Data Chip and the TV Scan.

The purpose of MUX II is to multiplex its 12 inputs to the six address

bits in the two time slices required for 4K x 1 16 pin RAMS.

The Memory Cycle Generator controls memory cycles generated by either the Z-80

or Scan Address Generator.  MREQ#, RD#, M1#, RFSH#, and A12-A15 are from the

Z-80.  A12-A15 are fed directly from the Z-80 because if they were brought

out of the microcycle decoder, they would arrive too late in the memory

cycle.  The RAS0 - RAS3 outputs are used to activate memory cycles.  In the

consumer game, only RAS0 is used to one bank of RAM (4K x 8).  In the commercial

game, all four RAS's are used to control four banks of RAM (16K x 8).  WRCTL and

LTCHD0 are control signals to the Data Chip.  WRCTL tells the Data Chip when to

place data to be written to memory on the memory data bus.  LTCHD0 tells

the Data Chip when valid data from RAM is present on the memory data bus.

As mentioned earlier, WAIT# is generated when the Z-80 and Scan Address

Generator both request memory at the same time.  WAIT# is also generated

for one cycle every time the Z-80 requests a memory access, even if there

is no conflict with the Scan Address.  This is because the microcycler

slows down Z-80 memory accesses.  The Z-80 address bus and data bus must

time share the microcycle bus so the Z-80 data reaches the microcycle bus

very late in the memory cycle.

The INT Generator generates two types of interrupts to the Z-80; Light

Pen and Screen interrupts.  A screen interrupt is generated when screen

interrupts are enabled and the TV scan completes a certain line on the

screen (from 0 to 255).  The line at which the interrupt will occur is

determined by the Z-80.  This interrupt can be used for timing since the

TV rescans every line once every 1/60th sec.  A light pen interrupt occurs

when the light pen interrupt is enabled and LIGHT PEN# goes low.  The

current scan address is saved in latches in the Scan Address Generator.

The Z-80 can read the contents of these latches to determine the scan

address at the time LIGHT PEN# was activated and thus the position of the

light pen on the screen.

The I/O Decode circuit is used during Z-80 input and output instructions.

Z-80 input instructions are used to read the scan address after light pen

interrupts.  Output instructions are used to enable the two interrupts and

set the line number for screen interrupts.

ADDRESS CHIP BLOCK DIAGRAM

--------------------------

DATA CHIP DESCRIPTION

---------------------

The TV Sync Generator uses 7M and 7M# (7.159090 Mhz square waves) to

generate NTSC standard sync and blank to be sent to the Video Generator.

It also generates HORIZ DR and VERT DR for synchronization with the

Address Chip.  HORIZ DR occurs once every horizontal line (63.5 usec),

and VERT DR occurs once every frame (16.6 msec).

The Shift Register loads parallel data from the memory data bus (MD0 - MD7)

and shifts it out of its two serial outputs.  The TV Sync Generator controls

when data is loaded or shifted.  In a consumer game, the two outputs of

the shift register are sent through MUX I to MUX II.  In a commercial

game, SERIAL 0 and SERIAL 1 are sent through MUX I and MUX II.  The

two bits from MUX I select 8 bits to be sent through MUX II to the Video

Generator.  These 8 bits then determine the analog voices of VIDEO, R-Y,

and B-Y.  2.5V is a 2.5V D C reference level.

The Clock Generator generates 0G and PX# from 7M.  These are the clocks

for the rest of the system.  The Frequency of PX# is half that of 7M

and the frequency of 0G is half that of PX#.

The Microcycle Generator generates the microcycle control bits, MC0 and

MC1 from IORQ#, MREQ#, RD#, and M1#, all from the Z-80.

In memory write cycles WRCTL is activated and the Memory Control circuit

generates DATEN#.  The Magic Function Generator takes the data from the

Z-80 on MUXD0 - D7 and transfers it to MD0 - MD7.  If a Magic write is

being done, the Magic Function Generator will modify the data as required

before it places it on the memory data bus.

A Magic write is a memory write cycle in which data is written to a

location, (X) from 0 to 16K.  All memory from 0 to 16K is ROM and cannot

be modified.  The data is modified by the Magic Function Generator and

is written to location X + 16K.  The way in which the data is modified is

determined by the 7 bits coming from the I/O registers.

In memory reads, data is transferred from MD0 - MD7 to MUXD0 - MUXD7.

Also, LTCHD0 is activated which causes the data from RAM to be latched

up in a register in the Magic Function Generator.  This latched data

is used in some magic functions.

The I/O registers are loaded by output instructions from the Z-80 just

as in the Address Chip.

DATA CHIP BLOCK DIAGRAM

-----------------------

I/O CHIP DESCRIPTION

--------------------

The Z-80 communicates with the I/O Chip through input and output

instructions.  The state of an 8 x 8 switch matrix can be read through

the Switch Scan circuit.  When an input instruction is executed, one

of the SO0-SO7 lines will be activated.  When a line is activated, the

switch matrix will feed back eight bits of data on SI0-SI7.  This data

is in turn fed to the Z-80 through MUXD0 - MUXD7.

The Z-80 can read the position of four potentiometers (pots) through the

A-D Converter circuit.  The pots are continuously scanned by the A-D

Converter and the results of the conversions are stored in a RAM in the

A-D Converter circuit.  The Z-80 simply reads this RAM with input

instructions.

The Z-80 loads data into the Music Processor with output instructions.

This data determines the characteristics of the audio that is generated.

The Music Processor is described in detail below.

I/O CHIP BLOCK DIAGRAM

----------------------

MUSIC PROCESSOR

---------------

The music processor can be divided into two sections.  The first section

generates the Master Oscillator Frequency and the second section uses the

Master Oscillator Frequency to generate tone frequencies and the analog

audio output.  The contents of all registers in the Music Processor are

set by output instructions from the Z-80.

Master Oscillator Frequency is a square wave whose frequency is determined

by the 8 binary inputs to the Master Oscillator.  This 8-bit word is the

sum of the contents of the Master Oscillator Register and the output

of the MUX.  The MUX is controlled by MUX REG.

If MUX REG contains 0, then data from the Vibrato System will be fed

through the MUX.  The two bits from the Vibrato Frequency Register

determine the frequency of the square wave output of the Low Frequency

Oscillator.  The 6-bit word at the output of the AND gates oscillates

between 0 and the contents of the Vibrato Register.  The frequency of

oscillation is determined by the contents of the Vibrato Frequency

Register.  The 6-bit word, along with two ground bits are fed through

the MUX to the Adder.  This causes the Master Oscillator Frequency to be

modulated between two values thus giving a Vibrato effect.

If MUX REG contains 1, then data from the Noise System will be fed

through the MUX.  The 8-bit word from the Noise Volume Register

determines which bits from the Noise Generator will be present at the

output of the AND gates.

If a bit in the Noise Volume Register is 0, then the corresponding

bit at the output of the AND gates will be 0.  If a bit in the Noise

Volume Register is 1, then the corresponding bit at the output of the

AND gates will be noise from the Noise Generator.  This 8-bit word is

sent through the MUX to the Adder.  The Master Oscillator Frequency is

modulated by noise.

In the second part of the Music Processor, the square wave from the

Master Oscillator is fed to three Tone Generator circuits which produce

square waves at their outputs.  The frequency of their outputs is

determined by the contents of their Tone Generator Register and Master

Oscillator Frequency.  The 4-bit words at the output of the AND gates

oscillate between 0 and the contents of the Tone Volume Register.  These

4-bit words are sent to D-A Converters whose outputs oscillate between

GND and a positive analog voltage determined by the contents of the Tone

Volume Register.

One Noise bit and four Noise Volume bits from the first section of the

Music Processor are fed to a set of AND gates.  This set of AND gates

operates the same way as the AND gates for the tones, except that the

Noise AM Register must contain a 1 for the outputs of the AND gates to

oscillate.  The analog outputs of the four D-A Converters are summed to

produce the single audio output.

MASTER OSCILLATOR BLOCK DIAGRAM

-------------------------------

TONE GENERATORS

---------------

CUSTOM CHIP TIMING

------------------

The following diagrams show the relationship of various signals

in the system during different types of operations.  Delays are

shown to be zero nsec from the clock edge which cause the transition.

The actual delay is given in "Electrical Specifications for Midway

Custom Circuits."

MUXD0 - MUXD7 is an 8-bit bidirectional address and data bus for

the custom chips.  By using this technique, 16 bits of address and

8 bits of data can be sent to the custom chips on 8 wires.  The

state of the bus is determined by MC0 and MC1 from the data chip

and RFSH# from the Z-80.

RFSH#    MC1     MC0

-----    ---     ---

L       L       L          A0 - A7 to custom chips

L       L       H          A0 - A7 to custom chips

L       H       L          A0 - A7 to custom chips

L       H       H          A0 - A7 to custom chips

H       L       L          A0 - A7 to custom chips

H       L       H          A8 - A15 to custom chips

H       H       L          D0 - D7 to custom chips

H       H       H          D0 - D7 from custom chips

MEMORY WRITE WITHOUT EXTRA WAIT STATE

-------------------------------------

MEMORY WRITE WITH VIDEO WAIT STATE

MEMORY READ WITHOUT EXTRA WAIT STATE

MEMORY READ WITH VIDEO WAIT STATE

---------------------------------

I/O READ FROM PORT 10H - 17H

----------------------------

I/O READ FROM OTHER THAN PORT 10H - 17H

---------------------------------------

I/O WRITE

---------

VIDEO TIMING

------------

The frequency of PX# is half that of 7M and the 0 is one-fourth 7M.

There are 455 cycles of 7M per horizontal line and 133 3/4 Phi cycles

per line.  Because of the extra 3/4 cycle, 0 must be resynchronized

at the beginning of each line.  This is done by stalling 0 for

3 cycles of 7M.  PX# is also stalled for the same amount of time.

The timing relationship is shown below.  The diagram also shows

the relationship of VERT DR to HORIZ DR.  The two RAS pulses shown

are the first two video RAS signals of a line, each line contains

forty.

RELATIONSHIP BETWEEN 7M, HORIZ DR, VERT DR, PHI G, PX AND RAS

-------------------------------------------------------------

RELATIONSHIP BETWEEN HORIZ DR, HORIZ BLANK, HORIZ SYNC AND COLOR BURST

----------------------------------------------------------------------

RELATIONSHIP BETWEEN VERTICAL SYNC, VERTICAL BLANK AND VERTICAL DRIVE

---------------------------------------------------------------------

- 1 -

ELECTRICAL SPECIFICATION FOR MIDWAY CUSTOM CIRCUITS

---------------------------------------------------

I. GENERAL SYSTEM PARAMETERS                       | REVISIONS:

| ---------

I. A.  Power Supplies                             | 1/14/77   N/C

--------------                             | 1/27/77   A  135

| 3/25/77   B

1.  VDD=+5.0V +/- 5%                       | 7/6/77    C

2.  VGG=+10.0V +/- 5%

3.  VSS=0.0V

I. B.  Timing Signals

--------------

1.  0 & 0#; Period = 560nsec, High time^* 240nsec to 260nsec.

0 & 0# have zero level crossover +1 volt -0 volts.

t_r, t_f^*                    less than 20nsec

2.  7M & 7M#; Period = 140nsec, High time^+ 50nsec to 70nsec

7M & 7M# have zero level crossover +1 volt -0 volt

t_r, t_f^+                     less than 15nsec

Dead time <= 5nsec

Max C Load = 20pf

+Note

1) High time is time clock at >=.6V.

2) Rise time from zero level to one level.

- 2 -

I. B.  (Continued)

*Note:

1. High time is time between 50% points.

2. Clock signals are generated by low power Shottky Logic

(series 74LS).  Full level swing on clock signals to be

achieved through external resistor to V_DD.  Zero level

.7V to 0V.

3. Rise time from zero level to .9V_DD.

I. C. Z80 Data Bus (MUXD0-MUXD7)

--------------------------

1.  Z80 Data Bus interface requires a three-state output/input

buffer.  The three states are defined below.

2.  Logic 0:  .5V + noise generated by chip, noise for address

chip is .15V @ -430uA

3.  Logic 1:  2.7V @ +70uA

4.  High Impedance:  Leakage at either logic 0 or 1 to be

less than 5uA.

5.  Transient Response:  Transition from High Impedance to

0 or 1 will be complete within 442nsec

of the 90% point of 0# of the last wait

state of input cycle or 442nsec of the

90% point of the 0 of the second wait state

of the interrupt acknowledge cycle.

The maximum load will be 80pf.  This

includes 14pfd for two custom chips.

6.  Exception:  The path through the Data chip connecting

the RAM bus with the Z80 bus shall introduce

a maximum of 160nsec of delay.

7.  The low address byte will be valid on the Z80 Data Bus

at least 62nsec before 0#.  The high address byte will

be valid at least 79nsec before 0#.  The data byte will be

valid 55nsec before 0#.

- 3 -

I. D.  RAM Data Bus (MD0-MD7) - Home Game

----------------------

1.  The RAM Data Bus will require three state logic buffers.

2.  Logic 0:   .5V @ -25uA

3.  Logic 1:  2.7V @ +25uA

4.  High Impedance: 5uA maximum leakage at either logic 0 or 1.

5.  Transient Response:  The outputs shall transition from High

Impedance to 0 or 1 within 120nsec of 7M.

The outputs shall transition from 1 or 0

to high impedance within 20nsec of 7M.

Maximum load will be 20pf.

I. E.  RAM Data Bus (MD0-MD7) - Commercial Game

----------------------

1.  The RAM Data Bus will require three state logic buffers.

2.  Logic 0:   .5V @ -200uA

3.  Logic 1:  2.7V @ +25uA

4.  High Impedance: 5uA maximum leakage at either logic 0 or 1.

5.  Transient Response:  The outputs shall transition from High

Impedance to 0 or 1 within 120nsec of

7M.  The output shall transition from

1 or 0 to High Impedance within 2nsec

of 7M.  Maximum load will be 10pf.

I. F.  Ambient operating temperature >= 0'C, <= 55'C

I. G.  Storage temperature >= -65'C, <= 150'C.

I. H.  Packing 40 pin plastic.

II. CUSTOM CIRCUIT SPECIFICATION

This specification defines the terminal characteristics for

each of the custom circuits.  These specifications shall take

precedence in case of conflict.  All 0 references refer to

the 0 and 0# inputs to the address and I/O chip.

- 4 -

II.  A.  Data Chip

---------

1. Input Pin List    V0    V1    t_d (Low)^1  t_d (High)^1  Ref.

--    --    -----------  -----------   ----

(V)   (V)     (nsec)       (nsec)

MREQ#             .5    2.45     132            6         7M

RD#               .5    2.45      12            6         7M

IORQ#             .5    2.45     112          126         7M

7M                See Section I.B.

7M#               See Section I.B.

WRCTL#            .5    3.1       82           82         7M

M1#               .5    2.45      12           82         7M

LTCHDO            .5    3.1      120          120         7M

Serial 0          .5    2.45      30           30         7M

Serial 1          .5    2.45      30           30         7M

2. Power Supplies

See Section I. A.

3. Bus Connections

MXD0      See Z80 Data Bus Spec. Section I.C.

MXD1       "                              "

MXD2       "                              "

MXD3       "                              "

MXD4       "                              "

MXD5       "                              "

MXD6       "                              "

MXD7       "                              "

MD0       See RAM Data Bus Spec Section I.D.

MD1        "                              "

MD2        "                              "

MD3        "                              "

MD4        "                              "

MD5        "                              "

MD6        "                              "

MD7        "                              "

- 5 -

4. Outputs    V0        I0    V1     I1     CAP    t_p    Ref.

--        --    --     --     ---    ----   ----

(V)      (uA)   (V)    (uA)   (pf)  (nsec)

VIDEO*      *                            10     100    7M

R-Y*        *                            10     600

B-Y*        *                            10     600

HORIZ DR   Note 4   400    2.7    20     20      20    7M

VERT DR    Note 4   400    2.7    20     20      20    7M

2.5V^6       --     --     --     --     --      DC

0          Note 4   400    2.7    20     10     100    7M

PXCLK#     Note 4   400    2.7    20     10     100    7M

MC0        Note 4   400    2.7    20     10     120    7M

MC1        Note 4   400    2.7    20     10     120    7M

DATEN#     Note 4   400    2.7    20     10      90    7M

*Video, R-Y, B-Y are analog outputs at 140nsec rate.  Video,

must switch from 10% to 90% of black to white in 140nsec.

R-Y and B-Y transitions not to exceed .6usec.

1  t_d (Low) and t_d (High) is maximum time in nsec except where a

minimum is shown.

2  For IORQ# Ref. to 0# t_d (Low)=132nsec t_d (High)=6nsec.

3  Serial 0 and Serial 1 will operate at 7MHz

4  .5 + noise generated by chip.

5. Tap on both resistor chains for a capacitor.  Will become test

input with voltage applied > 8V.

6  The Z80 0 is generated by this signal with a clock driver which

introduces a delay of <20nsec.

- 6 -

II. B.  I/O Chip

--------

1. Input Pin List    V0     V1    Ref     t_d (High)  t_d (Low)

--     --    ---     ---------   ---------

(nsec)      (nsec)

Reset             .5     2.45

MONOS             Note 1

RD#               .5     2.45  0 or 0#    166         172 0 or 0#

IORQ#             .5     2.45  0^6        146 0#      132 0

0                 See Section I.B.

0#                See Section I.B.

SI0               .5     3.3                          Note 3

SI1               .5     3.3                          Note 3

SI2               .5     3.3                          Note 3

SI3               .5     3.3                          Note 3

SI4               .5     3.3                          Note 3

SI5               .5     3.3                          Note 3

SI6               .5     3.3                          Note 3

SI7               .5     3.3                          Note 3

TEST              .5     5.0                           DC

2. Power Supplies

See Section I.A.

3. Bus Connections

MUXD0    See Z80 Data Bus Spec Section I.C.

MUXD1     "                             "

MUXD2     "                             "

MUXD3     "                             "

MUXD4     "                             "

MUXD5     "                             "

MUXD6     "                             "

MUXD7     "                             "

4. Outputs            V0     I0     V1      I1

--     --     --      --

(V)    (uA)   (V)    (uA)

Audio     Note 4  Fmax - 20KHz

Discharge Note 5   .5V    4V

SO0       Note 3  Note 7 200     4V     1650

SO1       Note 3  Note 7 200     4V     1650

SO2       Note 3  Note 7 200     4V     1650

SO3       Note 3  Note 7 200     4V     1650

SO4       Note 3  Note 7 200     4V     1650

SO5       Note 3  Note 7 200     4V     1650

SO6       Note 3  Note 7 200     4V     1650

SO7       Note 3  Note 7 200     4V     1650

POT 0     Note 2           5    V_DD-.5   50

POT 1     Note 2           5    V_DD-.5   50

POT 2     Note 2           5    V_DD-.5   50

POT 3     Note 2           5    V_DD-.5   50

- 7 -

Note 1    MONOS triggers at 2.1 volts +/- 2% +/- noise voltage

when the supply is 5.25V.

Note 2    Open source-Voltage measured with 0.2ma.

Note 3    Time from load of address into microcycle register

to date valid on MUX data bus from SI inputs

(data path through address decoder, out on SO

outputs, through closed switch and isolation diode,

into SI input to MUX Data Bus) shall be 2usec max.

Drop of isolation diode will be 0.7V max.  SO must

drive 2kohm in the high level.  Max C load of SO

shall be 300 pf.  SI input shall kill device

enabled by INPUT#.

Note 4    Audio voltage oscillates between 0V and one of the

following voltages; .33, .67, 1.00, 1.33, 1.67, 2.00,

2.33, 2.67, 3.00, 3.33, 3.67, 4.00, 4.33, 4.67, and

5.00.  These voltages should be +/- 6%.  The load shall

be 1000pf and 100kohm.

Note 5    Discharge is open drain to V_SS.  Discharges .01ufd

capacitor to .2V in 144usec.

Note 6    For IOREQ# Ref. to 0# t_d (Low)=152nsec t_d(High)=166nsec.

Note 7    .5V + noise generated by I/O chip.

Miscellaneous Timing

--------------------

Time for MO Adder - 20 max

- 8 -

II. C.  Address Chip

------------

1.  Input Pin List    V0     V1     t_pd (Low)  t_pd (High) REF

--     --     ----------  ----------  ---

(V)    (V)      (nsec)       (nsec)

RFSH#             .5     2.45     222 0        216      0

MREQ#             .5     2.45     152 0#       166      0 or 0#

RD#               .5     2.45     172 0 or 0#  166      0 or 0#

MI#               .5     2.45     176 0        242      0

A12^1             .5     2.45                           0

A13^1             .5     2.45                           0

A14^1             .5     2.45                           0

A15^1             .5     2.45                           0

IORQ#             .5     2.45     132 0        146      0#^2

LIGHT PEN#        .5     2.45     Asyn

TEST#             .5     5.0      DC

HORIZ. DR.        .5     2.45     Note 3                0#

VERT. DR.         .5     2.45     Note 4                0

0                 See Section I.B.

0#                See Section I.B.

2.  Power Supplies

See Section I.A.

3.  Bus Connections

MXD0        See Z80 Data Bus Spec Section I.E.

MXD1         "                             "

MXD2         "                             "

MXD3         "                             "

MXD4         "                             "

MXD5         "                             "

MXD6         "                             "

MXD7         "                             "

4.  Output     V0   I0    V1    I1    CAP T_pd(Low) T_pd(High)REF

--   --    --    --    --- --------- --------- ---

(V) (uA)   (V)  (uA)   (pf) (nsec)    (nsec)

LATCHD0  Note 7 Note 6 3.1 Note 6  10   280       140     0#^

WAIT#    Note 7  400   2.4  20     25   490       490     0#

MA0-MA5  Note 7  400   2.4  20     20   242       240     0# or 0

INT#     Note 7  400   2.4  20     25   490       572     0

RAS0-RAS3Note 7  400   2.4  20     20   382       382     0#

WRCTL#   Note 7 Note 6 3.1 Note 6  10   382       382     0#

1. Time from High Impedance to 1 or 0 is 200nsec. (from 0_1 of T_1)

2. For IORQ# Ref to 0# t_d (Low)=152nsec t_d (High)=166nsec. 0

3. Horizontal Drive time from low to high is 40nsec after 0#.

Time from high to low is 100nsec before rising edge of 0.

4. Vertical Drive will transition from low to high 40nsec after falling edge

of 0.  Its width will be 2.1 usec max, 1.54usec min.  It will go from

high to low 100nsec before falling edge of 0.

5. Reference t_pd (High) is 0.

6. MOS to MOS signal.

7. .5V + noise generated by Address Chip (.15V) = .65V

- 9 -

III. I/O MODE DECODE

I/O Parts

---------

HEX                OUT                     INPUT

---                ---                     -----

0           Color 0 Right

1           Color 1 Right

2           Color 2 Right

3           Color 3 Right

4           Color 0 Left

5           Color 1 Left

6           Color 2 Left

7           Color 3 Left

8           Consumer/Commercial      Intercept Feedback

9           Horiz Color Bndry

A           Vertical Blank

B           Color Block TX

C           Magic Reg

D           Interrupt Feedback

E           Interrupt Mode           Vertical Addr Feedback

F           Interrupt Line           Horizontal Addr Feedback

10           Tone Master OSC          SW Bank 0

11           Tone  A                  SW Bank 1

12           Tone  B                  SW Bank 2

13           Tone  C                  SW BANK 3

14           Tremolo                  SW BANK 4

15           Tone C Volume            SW BANK 5

16           Tone A,B Volume          SW BANK 6

17           Noise Volume             SW BANK 7

18           Sound Block TX

19

1A

1B

1C                                    Pot 0

1D                                    Pot 1

1E                                    Pot 2

1F                                    Pot 3

20

21

22

23

24

.

.

2F

End of 'Nutting' Manual - Continues with ROM Source

This page intentionally left blank for double-sided print purposes

Feb 08 16:23 2002	bally.h	 Page 1

1:			  ;  BALLY.H - Version 2.2

2:			  ;  Bally Astrocade Equates and Macros Header File

3:			  ;

4:			  ;  Retyped and proofread by Adam Trionfo and Lance F. Squire

5:			  ;  Version 1.0 - January 17, 2002

6:			  ;  Version 2.2 - February 6, 2002

7:			  ;    This ROM file contains the equates and macros that the

8:			  ;  Bally ROM requires for assembly (the header file is

9:			  ;  available separately too).  This file has been written to

10:			  ;  assemble with ZMAC 1.3 (a little known, freely distribut-

11:			  ;  able Z-80 assembler (with C source), that has a 25-year

12:			  ;  history. ZMAC can be compiled under just about any O.S.

13:			  ;  in existence, so try it out.  This file will probably

14:			  ;  require changes to be assembled under other assemblers.

15:			  ;

16:			  ;  To assemble your Z-80 source code using ZMAC:

17:			  ;

18:			  ;  zmac -d -o <outfile> -x <listfile> <filename>

19:			  ;

20:			  ;  For example, assemble this Astrocade Z-80 ROM file:

21:			  ;

22:			  ;  zmac -d -o BallyROM.bin -x BallyROM.lst BallyROM.asm

23:			  ;

24:			  ;    Currently the Listing file is full of 'Undeclared'

25:			  ;  errors.  When all of the source is typed-in, these will

26:			  ;  vanish. I'm leaving the others until all the source is

27:			  ;  re-typed.

28:			  ;

Feb 08 16:23 2002	bally.h	 Page 2

30:			  ; ***************************

31:			  ; * HOME VIDEO GAME EQUATES *

32:			  ; ***************************

33:			  ;

34:			  ;  ASSEMBLY CONTROL

35:			  ;

36:	0001          	XPNDON  EQU    1          ; ** SET TO 1 WHEN HARDWARE EXP

37:	0001          	NWHDWR  EQU    1          ; ** SET TO 1 WHEN NEW HARDWARE

38:			  ;

39:			  ;  GENERAL GOODIES

40:	4000          	NORMEM  EQU    4000H

41:	2000          	FIRSTC  EQU    2000H      ; FIRST ADDRESS IN CARTRIDGE

42:	0000          	SCREEN  EQU    0

43:	0028          	BYTEPL  EQU    40         ; BYTES PER LINE

44:	00A0          	BITSPL  EQU    160        ; BITS PER LINE

45:			  ;  STUFF IN SYSTEM DOPE VECTOR

46:	0200          	STIMER  EQU    200H       ; SECONDS AND GAME TIME,MUSIC

47:	0203          	CTIMER  EQU    203H       ; CUSTOM TIMERS

48:	0206          	FNTSYS  EQU    206H       ; SYSTEM FONT DESCRIPTOR

49:	020D          	FNTSML  EQU    20DH       ; SMALL FONT DESCRIPTOR

50:	0214          	ALKEYS  EQU    214H       ; KEYMASK OF ALL KEYS

51:	0218          	MENUST  EQU    218H       ; HEAD OF ONBOARD MENU

52:	021E          	MXSCR   EQU    21EH       ; ADDRESS OF 'MAX SCORE'

53:	0228          	NOPLAY  EQU    228H       ; ADDRESS OF '# OF PLAYERS'

54:	0235          	NOGAME  EQU    235H       ; ADDRESS OF '# OF GAMES'

55:			  ;  BITS IN PROCESSOR FLAG BYTE

56:	0007          	PSWSGN  EQU    7          ; SIGN BIT

57:	0006          	PSWZRO  EQU    6          ; ZERO BIT

58:	0002          	PSWPV   EQU    2          ; PARITY        OVERFLOW

59:	0000          	PSWCY   EQU    0          ; CARRY

60:			  ;  BITS IN GAME STATUS BYTE

61:	0000          	GSBTIM  EQU    0

62:	0001          	GSBSCR  EQU    1

63:	0007          	GSBEND  EQU    7

64:			  ;  STANDARD VECTOR DISPLACEMENTS AND BITS

65:	0000          	VBMR    EQU    0          ; MAGIC REGISTER

66:	0001          	VBSTAT  EQU    1          ; STATUS

67:	0002          	VBTIMB  EQU    2          ; TIME BASE

68:	0003          	VBDXL   EQU    3          ; DELTA X LO

69:	0004          	VBDXH   EQU    4          ; DELTA X HI

70:	0005          	VBXL    EQU    5          ; X COORD LO

71:	0006          	VBXH    EQU    6          ; X COORD HI

72:	0007          	VBXCHK  EQU    7          ; X CHECK FLAGS

73:	0008          	VBDYL   EQU    8          ; DELTA Y LO

74:	0009          	VBDYH   EQU    09H        ; DELTA Y HI

75:	000A          	VBYL    EQU    0AH        ; Y COORD LO

76:	000B          	VBYH    EQU    0BH        ; Y COORD HI

77:	000C          	VBYCHK  EQU    0CH        ; Y CHECK FLAGS

78:	000D          	VBOAL   EQU    0DH        ; OLD ADDRESS OF L.O.

79:	000E          	VBOAH   EQU    0EH        ; OLD ADDRESS OF H.O.

80:			  ;  DISPLACEMENTS FROM START OF COORDINATE AREA

81:	0000          	VBDCL   EQU    0          ; LO DELTA

82:	0001          	VBDCH   EQU    1          ; HI DELTA

83:	0002          	VBCL    EQU    2          ; LO COORD

84:	0003          	VBCH    EQU    3          ; HI COORD

85:	0004          	VBCCHK  EQU    4          ; CHECK BITS

Feb 08 16:23 2002	bally.h	 Page 3

86:			  ;  BITS IN STATUS BYTE

87:	0007          	VBSACT  EQU    7          ; VECTOR ACTIVE STATUS

88:	0006          	VBBLNK  EQU    6          ; BLANK STATUS

89:			  ;  BITS IN CHECK BIT MASK

90:	0000          	VBCLMT  EQU    0          ; DO LIMIT CHECKING

91:	0001          	VBCREV  EQU    1          ; REVERSE DELTA ON LIMIT ATTAIN

92:	0003          	VBCLAT  EQU    3          ; COORDINATE IS AT LIMIT

93:			  ;  FONT TABLE DISPLACEMENTS FOR NEW CHARACTER DISPLAY ROU

94:	0000          	FTBASE  EQU    0          ; BASE CHARACTER

95:	0001          	FTFSX   EQU    1          ; X FRAME SIZE

96:	0002          	FTFSY   EQU    2          ; Y FRAME SIZE

97:	0003          	FTBYTE  EQU    3          ; X SIZE FOR CHAR IN BYTES

98:	0004          	FTYSIZ  EQU    4          ; Y SIZE IN BITS

99:	0005          	FTPTL   EQU    5          ; PATTERN TABLE ADDRESS LO

100:	0006          	FTPTH   EQU    6          ; PATTERN TABLE ADDRESS HI

101:			  ;  BITS FOR MAGIC REGISTER     WRITE OPTION BYTE

102:	0006          	MRFLOP  EQU    6          ; WRITE WITH FLOP

103:	0005          	MRXOR   EQU    5          ; WRITE WITH EXCLUSIVE OR

104:	0004          	MROR    EQU    4          ; WRITE WITH OR

105:	0003          	MRXPND  EQU    3          ; WRITE WITH EXPAND

106:	0002          	MRROT   EQU    2          ; WRITE WITH ROTATE

107:	0003          	MRSHFT  EQU    03H        ; MASK OF SHIFT AMOUNT

108:			  ;  BITS OF CONTROL HANDLE INPUT PORT

109:	0004          	CHTRIG  EQU    4          ; TRIGGER

110:	0003          	CHRIGH  EQU    3          ; JOYSTICK RIGHT

111:	0002          	CHLEFT  EQU    2          ; JOYSTICK LEFT

112:	0001          	CHDOWN  EQU    1          ; DOWN

113:	0000          	CHUP    EQU    0          ; UP

114:			  ; CONTEXT BLOCK REGISTER DISPLACEMENTS

115:	0000          	CBIYL   EQU    0          ; IY

116:	0001          	CBIYH   EQU    1

117:	0002          	CBIXL   EQU    2          ; IX

118:	0003          	CBIXH   EQU    3

119:	0004          	CBE     EQU    4          ; DE

120:	0005          	CBD     EQU    5

121:	0006          	CBC     EQU    6          ; BC

122:	0007          	CBB     EQU    7

123:	0008          	CBFLAG  EQU    8          ; AF

124:	0009          	CBA     EQU    9

125:	000A          	CBL     EQU    0AH        ; HL

126:	000B          	CBH     EQU    0BH

127:			  ;  SENTRY RETURN CODES EQUATES:

128:	0000          	SNUL    EQU    0          ; NOTHING HAPPENED

129:	0001          	SCT0    EQU    1          ; COUNTER-TIMER 1 THRU 8

130:	0002          	SCT1    EQU    2

131:	0003          	SCT2    EQU    3

132:	0004          	SCT3    EQU    4

133:	0005          	SCT4    EQU    5

134:	0006          	SCT5    EQU    6

135:	0007          	SCT6    EQU    7

136:	0008          	SCT7    EQU    8

137:	0009          	SF0     EQU    9          ; FLAG BIT 0

138:	000A          	SF1     EQU    0AH

139:	000B          	SF2     EQU    0BH

140:	000C          	SF3     EQU    0CH

141:	000D          	SF4     EQU    0DH

Feb 08 16:23 2002	bally.h	 Page 4

142:	000E          	SF5     EQU    0EH

143:	000F          	SF6     EQU    0FH

144:	0010          	SF7     EQU    10H

145:	0011          	SSEC    EQU    11H        ; SECONDS TIMER HAS COUNTED DOWN

146:	0013          	SKYD    EQU    13H        ; KEY IS DOWN

147:	0012          	SKYU    EQU    12H        ; YES IS UP

148:	001C          	SP0     EQU    1CH        ; POT IS 0

149:	001D          	SP1     EQU    1DH        ; POT IS 1

150:	001E          	SP2     EQU    1EH        ; POT IS 2

151:	001F          	SP3     EQU    1FH        ; POT IS 3

152:	0014          	ST0     EQU    14H        ; TRIGGER 0

153:	0015          	SJ0     EQU    15H        ; JOYSTICK 0

154:	0016          	ST1     EQU    16H        ; SIMILARLY FOR 1-3

155:	0017          	SJ1     EQU    17H

156:	0018          	ST2     EQU    18H

157:	0019          	SJ2     EQU    19H

158:	001A          	ST3     EQU    1AH

159:	001B          	SJ3     EQU    1BH

Feb 08 16:23 2002	bally.h	 Page 5

161:			  ; ********************************

162:			  ; * HOME VIDEO GAME PORT EQUATES *

163:			  ; ********************************

164:			  ; OUTPUT PORTS FOR VIRTUAL COLOR

165:	0000          	COL0R   EQU    0          ; COLOR 0 RIGHT

166:	0001          	COL1R   EQU    1          ; COLOR 1 RIGHT

167:	0002          	COL2R   EQU    2          ; COLOR 2 RIGHT

168:	0003          	COL3R   EQU    3          ; COLOR 3 RIGHT

169:	0004          	COL0L   EQU    4          ; COLOR 0 LEFT

170:	0005          	COL1L   EQU    5          ; COLOR 1 LEFT

171:	0006          	COL2L   EQU    6          ; COLOR 2 LEFT

172:	0007          	COL3L   EQU    7          ; COLOR 3 LEFT

173:	000B          	COLBX   EQU    0BH        ; COLOR BLOCK OUTPUT PORT

174:	0009          	HORCB   EQU    9          ; HORIZONTAL COLOR BOUNDARY

175:	000A          	VERBL   EQU    0AH        ; VERTICAL BLANKING LINE

176:			  ; OUTPUT PORTS FOR MUSIC AND SOUNDS

177:	0010          	TONMO   EQU    10H        ; TONE MASTER OSCILLATOR

178:	0011          	TONEA   EQU    11H        ; TONE A OSC.

179:	0012          	TONEB   EQU    12H        ; TONE B OSC.

180:	0013          	TONEC   EQU    13H        ; TONE C OSC.

181:	0014          	VIBRA   EQU    14H        ; VIBRATO

182:	0016          	VOLAB   EQU    16H        ; TONES A,B VOLUME

183:	0015          	VOLC    EQU    15H        ; TONE C VOLUME

184:	0017          	VOLN    EQU    17H        ; NOISE VOLUME

185:	0018          	SNDBX   EQU    18H        ; SOUND BLOCK OUTPUT PORT

186:			  ; INTERRUPT AND CONTROL OUTPUT PORTS

187:	000D          	INFBK   EQU    0DH        ; INTERRUPT FEEDBACK

188:	000E          	INMOD   EQU    0EH        ; INTERRUPT MODE

189:	000F          	INLIN   EQU    0FH        ; INTERRUPT LINE

190:	0008          	CONCM   EQU    8          ; CONSUMER      COMMERCIAL

191:	000C          	MAGIC   EQU    0CH        ; MAGIC REGISTER

192:	0019          	XPAND   EQU    19H        ; EXPANDER PIXEL DEFINITION PORT

193:			  ; INTERRUPT AND INTERCEPT INPUT PORTS

194:	0008          	INTST   EQU    8          ; INTERCEPT STATUS

195:	000E          	VERAF   EQU    0EH        ; VERTICAL ADDRESS FEEDBACK

196:	000F          	HORAF   EQU    0FH        ; HORIZONTAL ADDRESS FEEDBACK

197:			  ; HAND CONTROL INPUT PORTS

198:	0010          	SW0     EQU    10H        ; PLAYER 0 HAND CONTROL

199:	0011          	SW1     EQU    11H        ; PLAYER 1 HAND CONTROL

200:	0012          	SW2     EQU    12H        ; PLAYER 2 HAND CONTROL

201:	0013          	SW3     EQU    13H        ; PLAYER 3 HAND CONTROL

202:	001C          	POT0    EQU    1CH        ; PLAYER 0 POT

203:	001D          	POT1    EQU    1DH        ; PLAYER 1 POT

204:	001E          	POT2    EQU    1EH        ; PLAYER 2 POT

205:	001F          	POT3    EQU    1FH        ; PLAYER 3 POT

206:			  ; KEYBOARD INPUT PORTS

207:	0014          	KEY0    EQU    14H        ; KEYBOARD COLUMN 0

208:	0015          	KEY1    EQU    15H        ; KEYBOARD COLUMN 1

209:	0016          	KEY2    EQU    16H        ; KEYBOARD COLUMN 2

210:	0017          	KEY3    EQU    17H        ; KEYBOARD COLUMN 3

Feb 08 16:23 2002	bally.h	 Page 6

212:			  ; ***************************************

213:			  ; * HOME VIDEO GAME SYSTEM CALL INDEXES *

214:			  ; ***************************************

215:			  ; USER PROGRAM INTERFACE

216:	0000          	UPISTR  EQU    0

217:	0000          	INTPC   EQU    UPISTR     ; INTERPRET WITH CONTEXT CREATE

218:	0002          	XINTC   EQU    INTPC+2    ; EXIT INTERPRETER WITH CONTEXT

219:	0004          	RCALL   EQU    XINTC+2    ; CALL ASM LANGUAGE SUBROUTINE

220:	0006          	MCALL   EQU    RCALL+2    ; CALL INTERPRETER SUBROUTINE

221:	0008          	MRET    EQU    MCALL+2    ; RETURN FROM INTERPRETER SUBRO

222:	000A          	MJUMP   EQU    MRET+2     ; MACRO JUMP

223:	000C          	SUCK    EQU    MJUMP+2    ; SUCK INLINE ARGS INTO CB

224:			  ; SCHEDULER ROUTINES

225:	000C          	SCHEDR  EQU    SUCK

226:	000E          	ACTINT  EQU    SCHEDR+2   ; SET SUB TIMER

227:	0010          	DECCTS  EQU    ACTINT+2   ; DEC CT'S UNDER MASK

228:			  ; MUSIC AND SOUNDS

229:	0012          	MUZAK   EQU    DECCTS+2

230:	0012          	BMUSIC  EQU    MUZAK      ; BEGIN PLAYING MUSIC

231:	0014          	EMUSIC  EQU    BMUSIC+2   ; STOP PLAYING MUSIC

232:			  ; SCREEN HANDLER ROUTINES

233:	0016          	SCRSTR  EQU    EMUSIC+2

234:	0016          	SETOUT  EQU    SCRSTR     ; SET SCREEN SIZE

235:	0018          	COLSET  EQU    SETOUT+2   ; SET COLORS

236:	001A          	FILL    EQU    COLSET+2   ; FILL MEMORY WITH DAT

237:	001C          	RECTAN  EQU    FILL+2     ; PAINT RECTANGLE

238:	001E          	VWRITR  EQU    RECTAN+2   ; WRITE RELATIVE FROM VECTOR

239:	0020          	WRITR   EQU    VWRITR+2   ; WRITE RELATIVE

240:	0022          	WRITP   EQU    WRITR+2    ; WRITE WITH PATTERN SIZE LOOKUP

241:	0024          	WRIT    EQU    WRITP+2    ; WRITE WITH SIZES PROVIDED

242:	0026          	WRITA   EQU    WRIT+2     ; WRITE ABSOLUTE

243:	0028          	VBLANK  EQU    WRITA+2    ; BLANK AREA FROM VECTOR

244:	002A          	BLANK   EQU    VBLANK+2   ; BLANK AREA

245:	002C          	SAVE    EQU    BLANK+2    ; SAVE AREA

246:	002E          	RESTOR  EQU    SAVE+2     ; RESTORE AREA

247:	0030          	SCROLL  EQU    RESTOR+2   ; SCROLL AREA OF SCREEN

248:			  ;

249:	0032          	CHRDIS  EQU    SCROLL+2   ; NEW DISPLAY CHARACTER

250:	0034          	STRDIS  EQU    CHRDIS+2   ; NEW DISPLAY STRING

251:	0036          	DISNUM  EQU    STRDIS+2   ; DISPLAY NUMBER

252:			  ;

253:	0038          	RELABS  EQU    DISNUM+2   ; RELATIVE TO ABSOLUTE CONVERSI

254:	003A          	RELAB1  EQU    RELABS+2   ; NONMAGIC RELABS

255:	003C          	VECTC   EQU    RELAB1+2   ; VECTOR SINGLE COORDINATE

256:	003E          	VECT    EQU    VECTC+2    ; VECTOR COORDINATE PAIR

257:			  ; HUMAN INTERFACE ROUTINES

258:	0040          	HUMANR  EQU    VECT +2

259:	0040          	KCTASC  EQU    HUMANR     ; KEY CODE TO ASCII

260:	0042          	SENTRY  EQU    KCTASC+2   ; SENSE TRANSITION

261:	0044          	DOIT    EQU    SENTRY+2   ; BRANCH TO TRANSITION HANDLER

262:	0046          	DOITB   EQU    DOIT+2     ; USE B INSTEAD OF A

263:	0048          	PIZBRK  EQU    DOITB+2    ; TAKE A BREAK

264:	004A          	MENU    EQU    PIZBRK+2   ; DISPLAY A MENU

265:	004C          	GETPAR  EQU    MENU+2     ; GET GAME PARAMENTER FROM USER

266:	004E          	GETNUM  EQU    GETPAR+2   ; GET NUMBER FROM USER

267:	0050          	PAWS    EQU    GETNUM+2   ; PAUSE

Feb 08 16:23 2002	bally.h	 Page 7

268:	0052          	DISTIM  EQU    PAWS+2     ; DISPLAY TIME

269:	0054          	INCSCR  EQU    DISTIM+2   ; INC SCORE

270:			  ; MATH ROUTINES

271:	0056          	MATH    EQU    INCSCR+2

272:	0056          	INDEXN  EQU    MATH       ; INDEX NIBBLE

273:	0058          	STOREN  EQU    INDEXN+2   ;

274:	005A          	INDEXW  EQU    STOREN+2   ; INDEX WORD

275:	005C          	INDEXB  EQU    INDEXW+2   ; INDEX BYTE

276:	005E          	MOVE    EQU    INDEXB+2   ; BLOCK TRANSFER

277:	0060          	SHIFTU  EQU    MOVE+2     ; SHIFT UP A DIGIT

278:	0062          	BCDADD  EQU    SHIFTU+2   ; BCD ADD

279:	0064          	BCDSUB  EQU    BCDADD+2   ; BCD SUBTRACT

280:	0066          	BCDMUL  EQU    BCDSUB+2   ; BCD MULTIPLY

281:	0068          	BCDDIV  EQU    BCDMUL+2   ; BCD DIVIDE

282:	006A          	BCDCHS  EQU    BCDDIV+2   ; BCD CHANGE SIGN

283:	006C          	BCDNEG  EQU    BCDCHS+2   ; BCD NEGATE

284:	006E          	DADD    EQU    BCDNEG+2   ; DECIMAL ADD

285:	0070          	DSMG    EQU    DADD+2     ; CONVERT TO SIGN MAGNITUDE

286:	0072          	DABS    EQU    DSMG+2     ; DECIMAL ABSOLUTE VALUE

287:	0074          	NEGT    EQU    DABS+2     ; NEGATE

288:	0076          	RANGED  EQU    NEGT+2     ; RANGED RANDOM NUMBER

289:	0078          	QUIT    EQU    RANGED+2   ; QUIT CASSETTE EXECUTION

290:	007A          	SETB    EQU    QUIT+2     ; SET BYTE

291:	007C          	SETW    EQU    SETB+2     ; SET WORD

292:	007E          	MSKTD   EQU    SETW+2     ; MASK TO DELTAS

Feb 08 16:23 2002	bally.h	 Page 8

294:			  ; **********

295:			  ; * MACROS *

296:			  ; **********

297:			  ; MACROS TO DEFINE PATTERNS

298:			DEF2    MACRO  AA, AB

299:			        DEFB   AA

300:			        DEFB   AB

301:			        ENDM

302:			DEF3    MACRO  BA, BB, BCC

303:			        DEFB   BA

304:			        DEFB   BB

305:			        DEFB   BCC  ; 'BC' reserved, so used 'BCC'

306:			        ENDM

307:			DEF4    MACRO  CA, CB, CC, CD

308:			        DEFB   CA

309:			        DEFB   CB

310:			        DEFB   CC

311:			        DEFB   CD

312:			        ENDM

313:			DEF5    MACRO  DA, DBB, DC, DD, DEE

314:			        DEFB   DA

315:			        DEFB   DBB  ; 'DB' reserved, so used 'DBB'

316:			        DEFB   DC

317:			        DEFB   DD

318:			        DEFB   DEE  ; 'DE' reserved, so used 'DEE'

319:			        ENDM

320:			DEF6    MACRO  EA, EB, EC, ED, EE, EF

321:			        DEFB   EA

322:			        DEFB   EB

323:			        DEFB   EC

324:			        DEFB   ED

325:			        DEFB   EE

326:			        DEFB   EF

327:			        ENDM

328:			DEF8    MACRO  GA, GB, GC, GD, GEE, GF, GG, GH

329:			        DEFB   GA

330:			        DEFB   GB

331:			        DEFB   GC

332:			        DEFB   GD

333:			        DEFB   GEE  ; 'GE' reserved, so used 'GEE'

334:			        DEFB   GF

335:			        DEFB   GG

336:			        DEFB   GH

337:			        ENDM

338:			  ; MACROS TO COMPUTE CONSTANT SCREEN ADDRESSES

339:			XYRELL  MACRO  p1, p2, p3  ; RELATIVE LOAD

340:			        LD     p1,. RES. (p3). SHL. 8+(p2)

341:			        ENDM

342:			 ; MACRO TO GENERATE SYSTEM CALL

343:			SYSTEM  MACRO  NUMBA

344:			        RST    56

345:			        DEFB   NUMBA

346:			        IF     NUMBA = INTPC

347:			INTPCC   DEFL   1

348:			        ENDIF

349:			        ENDM

Feb 08 16:23 2002	bally.h	 Page 9

350:			  ; MACRO TO GENERATE SYSTEM CALL WITH SUCK OPTION ON

351:			SYSSUK  MACRO  UMBA

352:			        RST    56

353:			        DEFB   UMBA+1

354:			        IF     UMBA = INTPC

355:			INTPCC  DEFL   1

356:			        ENDIF

357:			        ENDM

358:			  ; MACROS TO GENERATE MACRO INSTRUCTION CALLS

359:			  ; FILL SCREEN WITH CONSTANT DATA (was 'FILL?')

360:			FILLq   MACRO  START, NBYTES, DATA

361:			        DEFB   FILL+1

362:			        DEFW   START

363:			        DEFW   NBYTES

364:			        DEFB   DATA

365:			        ENDM

366:			  ; EXIT INTERPRETER WITH CONTEXT RESTORE

367:			EXIT    MACRO

368:			        DEFB   XINTC

369:			INTPCC  DEFL   0

370:			        ENDM

371:			  ; INTERPRET WITH INLINE SUCK

372:			DO      MACRO  CID

373:			        DEFB   CID+1

374:			        ENDM

375:			  ; INTERPRET WITHOUT INLINE SUCK

376:			DONT    MACRO  CID

377:			        DEFB   CID

378:			        ENDM

379:			  ; MACRO CALL FROM DOIT TABLE

380:	00C0          	ENDx    EQU    0C0H

381:			MC      MACRO  AA, BB, EE

382:			        DEFB   AA+80H

383:			        DEFW   BB

384:			        IF     EE

385:			        DEFB   EE

386:			        ENDIF

387:			        ENDM

388:			  ; REAL CALL FROM DOIT TABLE

389:			RC      MACRO  AA, BB, EE

390:			        DEFB   AA+40H

391:			        DEFW   BB

392:			        IF     EE

393:			        DEFB   EE

394:			        ENDIF

395:			        ENDM

396:			  ; REAL JUMP FROM DOIT TABLE

397:			JMPd    MACRO  AA, BB, EE

398:			        DEFB   AA

399:			        DEFW   BB

400:			        IF     EE

401:			        DEFB   EE

402:			        ENDIF

403:			        ENDM

404:			  ; DISPLAY A STRING

405:			TEXTD   MACRO  AA, BB, CC, DD

Feb 08 16:23 2002	bally.h	 Page 10

406:			        DEFB   STRDIS+1

407:			        DEFB   BB

408:			        DEFB   CC

409:			        DEFB   DD

410:			        DEFW   AA

411:			        ENDM

413:			  ;**************

414:			  ; MUSIC MACROS

415:			  ; NOTE DURATION, FREQ(S)

416:			NOTE1   MACRO  DUR, N1

417:			        DEFB   (DUR)&(7FH)

418:			        DEFB   N1

419:			        ENDM

420:			NOTE2   MACRO  DUR, N1, N2

421:			        DEFB   (DUR)&(7FH)

422:			        DEFB   N1

423:			        DEFB   N2

424:			        ENDM

425:			NOTE3   MACRO  DUR, N1, N2, N3

426:			        DEFB   DUR

427:			        DEFB   N1

428:			        DEFB   N2

429:			        DEFB   N3

430:			        ENDM

431:			NOTE4   MACRO  DUR, N1, N2, N3, N4

432:			        DEFB   DUR

433:			        DEFB   N1

434:			        DEFB   N2

435:			        DEFB   N3

436:			        DEFB   N4

437:			        ENDM

438:			NOTE5   MACRO  DUR, N1, N2, N3, N4, N5

439:			        DEFB   DUR

440:			        DEFB   N1

441:			        DEFB   N2

442:			        DEFB   N3

443:			        DEFB   N4

444:			        DEFB   N5

445:			        ENDM

446:			MASTER  MACRO  OFFSET

447:			        DEFB   80H

448:			        DEFB   OFFSET

449:			        ENDM

450:			  ; STUFF OUTPUT PORT#, DATA  OR

451:			  ; OUTPUT SNDBX, DATA10, D11,..., DATA17

452:			OUTPUT  MACRO  PORT, D0, D1, D2, D3, D4, D5, D6, D7

453:			        IF     .NOT. (PORT=18H)

454:			        DEFB   80H+((PORT)&(7FH))

455:			        DEFB   D0

456:			        ENDIF

457:			        IF     PORT=18H

458:			        DEFB   88H

Feb 08 16:23 2002	bally.h	 Page 11

459:			        DEF8   D7, D6 ,D5, D4, D3, D2, D1, D0

460:			        ENDIF

461:			        ENDM

462:			  ; SET VOICE BYTE

463:			  ; THE FORMAT OF THE VOICE BYTE IS

464:			  ; *I*A*I*B*I*C*V*N

465:			  ; WHERE N = LOAD NOISE WITH DATA AT PC AND INC PC

466:			  ; V = LOAD VIBRATO AND INC PC

467:			  ; I = INC PC

468:			  ; A,B,C = LOAD TONE A,B,C WITH DATA AT PC

469:			VOICEM  MACRO  MASK  ;  'VOICES' TO 'VOICEM'

470:			        DEFB   90H

471:			        DEFB   MASK

472:			        ENDM

473:			; PUSH NUMBER ONTO STACK

474:			PUSHN   MACRO  NUMB

475:			        DEFB   0A0H+((NUMB-1). AND. 0FH)

476:			        ENDM

477:			  ; SET VOLUMES

478:			VOLUME  MACRO  P1, P2

479:			        DEFB   0B0H

480:			        DEFB   P1

481:			        DEFB   P2

482:			        ENDM

483:			; CALL RELATIVE 0-15 BEYOND SELF+1

484:			CREL    MACRO  BY

485:			        DEFB   0D0H+(BY.AND.0FH)

486:			        ENDM

487:			; DEC STACK TOP AND JNZ

488:			DSJNZ   MACRO  ADD_IT

489:			        DEFB   0C0H

490:			        DEFW   ADD_IT

491:			        ENDM

492:			; FLIP LEGATO  STACATO

493:			LEGSTA  MACRO

494:			        DEFB   0E0H

495:			        ENDM

496:			REST    MACRO  TIME

497:			        DEFB   0E1H

498:			        DEFB   TIME

499:			        ENDM

500:			QUIET   MACRO

501:			        DEFB   0F0H

502:			        ENDM

503:			  ; *****************

504:			  ; * MUSIC EQUATES *

505:			  ; *****************

506:			  ; NOTE VALUES

507:	00FD          	G0      EQU    253

508:	00EE          	GS0     EQU    238

509:	00E1          	A0      EQU    225

510:	00D4          	AS0     EQU    212

511:	00C8          	B0      EQU    200

512:	00BD          	C1      EQU    189

513:	00B2          	CS1     EQU    178

514:	00A8          	D1      EQU    168

Feb 08 16:23 2002	bally.h	 Page 12

515:	009F          	DS1     EQU    159

516:	0096          	E1      EQU    150

517:	008D          	F1      EQU    141

518:	0085          	FS1     EQU    133

519:	007E          	G1      EQU    126

520:	0077          	GS1     EQU    119

521:	0070          	A1      EQU    112

522:	006A          	AS1     EQU    106

523:	0064          	B1      EQU    100

524:	005E          	C2      EQU    94

525:	0059          	CS2     EQU    89

526:	0054          	D2      EQU    84

527:	004F          	DS2     EQU    79

528:	004A          	E2      EQU    74

529:	0046          	F2      EQU    70

530:	0042          	FS2     EQU    66

531:	003E          	G2      EQU    62

532:	003B          	GS2     EQU    59

533:	0037          	A2      EQU    55

534:	0034          	AS2     EQU    52

535:	0031          	B2      EQU    49

536:	002E          	C3      EQU    46

537:	002C          	CS3     EQU    44

538:	0029          	D3      EQU    41

539:	0027          	DS3     EQU    39

540:	0025          	E3      EQU    37

541:	0022          	F3      EQU    34

542:	0020          	FS3     EQU    32

543:	001F          	G3      EQU    31

544:	001D          	GS3     EQU    29

545:	001B          	A3      EQU    27

546:	001A          	AS3     EQU    26

547:	0018          	B3      EQU    24

548:	0017          	C4      EQU    23

549:	0015          	CS4     EQU    21

550:	0014          	D4      EQU    20

551:	0013          	DS4     EQU    19

552:	0012          	E4      EQU    18

553:	0011          	F4      EQU    17

554:	0010          	FS4     EQU    16

555:	000F          	G4      EQU    15

556:	000E          	GS4     EQU    14

557:	000D          	A4      EQU    13

558:	000B          	C5      EQU    11

559:	000A          	CS5     EQU    10

560:	0009          	DS5     EQU    9

561:	0008          	F5      EQU    8

562:	0007          	G5      EQU    7

563:	0006          	A5      EQU    6

564:	0005          	C6      EQU    5

565:	0004          	DS6     EQU    4

566:	0003          	G6      EQU    3

567:	0002          	C7      EQU    2

568:	0001          	G7      EQU    1

569:	0000          	G8      EQU    0

570:			  ; MASTER OSCILATOR OFFSETS

Feb 08 16:23 2002	bally.h	 Page 13

571:	00FE          	OB0     EQU    254

572:	00F1          	OC0     EQU    241

573:	00D6          	OD1     EQU    214

574:	00BF          	OE1     EQU    191

575:	00B4          	OF1     EQU    180

576:	00A0          	OG1     EQU    160

577:	008F          	OA1     EQU    143

578:	0047          	OA2     EQU    71

579:	0023          	OA3     EQU    35

580:	0011          	OA4     EQU    17

581:	0008          	OA5     EQU    8

Feb 08 16:23 2002	bally.h	 Page 14

583:			  ; ***************************

584:			  ; * SYSTEM RAM MEMORY CELLS *

585:			  ; ***************************

586:	0FFF          	WASTE   EQU    0FFFH

587:	0FFF          	WASTER  EQU    WASTE

588:			  ;

589:			  ; THE FOLLOWING ORG SHOULD BE SET TO THE VALUE OF

590:			  ; THE TAG 'SYSRAM', THIS WILL CAUSE SYSTEM RAM

591:			  ; TO RESIDE AT THE HIGEST POSSIBLE ADDRESS

592:			  ;

593:			;        ORG    4FC8H

594:			;        DEFS   6          ; GOT SOME LEFT STILL

595:	4FCE          	BEGRAM  EQU    4FCEH

596:			  ; USED BY MUSIC PROCESSOR

597:	4FCE          	MUZPC   EQU    4FCEH      ; MUSIC PROGRAM COUNTER

598:	4FD0          	MUZSP   EQU    4FD0H      ; MUSIC STACK POINTER

599:	4FD2          	PVOLAB  EQU    4FD2H      ; PRESET VOLUME FOR TONES A AND B

600:	4FD3          	PVOLMC  EQU    4FD3H      ; PRESET VOLUME FOR MASTER OSC

601:	4FD4          	VOICES  EQU    4FD4H      ; MUSIC VOICES

602:			  ; COUNTER TIMERS (USED BY DECCTS,ACTINT,CTIMER)

603:	4FD5          	CT0     EQU    4FD5H      ; COUNTER TIMER 0

604:	4FD6          	CT1     EQU    4FD6H      ; 1

605:	4FD7          	CT2     EQU    4FD7H      ; 2

606:	4FD8          	CT3     EQU    4FD8H      ; 3

607:	4FD9          	CT4     EQU    4FD9H      ; 4

608:	4FDA          	CT5     EQU    4FDAH      ; 5

609:	4FDB          	CT6     EQU    4FDBH      ; 6

610:	4FDC          	CT7     EQU    4FDCH      ; 7

611:			  ;USED BY SENTRY TO TRACK CONTROLS

612:	4FDD          	CNT     EQU    4FDDH      ; COUNTER UPDATE&NUMBER TRACKING

613:	4FDE          	SEMI4S  EQU    4FDEH      ; FLAG BITS

614:	4FDF          	OPOT0   EQU    4FDFH      ; POT 0 TRACKING

615:	4FE0          	OPOT1   EQU    4FE0H      ; POT 1 TRACKING

616:	4FE1          	OPOT2   EQU    4FE1H      ; POT 2 TRACKING

617:	4FE2          	OPOT3   EQU    4FE2H      ; POT 3 TRACKING

618:	4FE3          	KEYSEX  EQU    4FE3H      ; KEYBOARD TRACKING BYTE

619:	4FE4          	OSW0    EQU    4FE4H      ; SWITCH 0 TRACKING

620:	4FE5          	OSW1    EQU    4FE5H      ; SWITCH 1 TRACKING

621:	4FE6          	OSW2    EQU    4FE6H      ; SWITCH 2 TRACKING

622:	4FE7          	OSW3    EQU    4FE7H      ; SWITCH 3 TRACKING

623:	4FE8          	COLLST  EQU    4FE8H      ; COLOR LIST ADDRESS FOR P.B.A

624:			  ; USED BY STIMER

625:	4FEA          	DURAT   EQU    4FEAH      ; NOTE DURATION

626:	4FEB          	TMR60   EQU    4FEBH      ; SIXTIETHS OF SEC

627:	4FEC          	TIMOUT  EQU    4FECH      ; BLAKOUT TIMER

628:	4FED          	GTSECS  EQU    4FEDH      ; GAME TIME SECONDS

629:	4FEE          	GTMINS  EQU    4FEEH      ; GAME TIME MINUTES

630:			  ; USED BY MENU

631:	4FEF          	RANSHT  EQU    4FEFH      ; RANDOM NUMBER SHIFT REGISTER

632:	4FF3          	NUMPLY  EQU    4FF3H      ; NUMBER OF PLAYERS

633:	4FF4          	ENDSCR  EQU    4FF4H      ; SCORE TO 'PLAY TO'

634:	4FF7          	MRLOCK  EQU    4FF7H      ; MAGIC REGISTER LOCK OUT FLAG

635:	4FF8          	GAMSTB  EQU    4FF8H      ; GAME STATUS BYTE

636:	4FF9          	PRIOR   EQU    4FF9H      ; MUSIC PROTECT FLAG

637:	4FFA          	SENFLG  EQU    4FFAH      ; SENTRY CONTROL SEIZURE FLAG

638:	4FFB          	UMARGT  EQU    4FFBH

Feb 08 16:23 2002	bally.h	 Page 15

639:	4FFD          	USERTB  EQU    4FFDH

640:	9FCD          	SYSRAM  EQU    (5000H-($-BEGRAM+1))

**** bally.h ****

Statistics:

426	symbols

0	bytes

0	macro calls

2744	macro bytes

0	invented symbols

Feb 08 16:23 2002	**  Symbol Table  **	 Page 16

Symbol Table:

a0             =  e1+    fntsml         = 20d+    ranged         =  76

a1             =  70+    fntsys         = 206+    ransht         =4fef+

a2             =  37+    fs1            =  85+    rc               521+

a3             =  1b+    fs2            =  42+    rcall          =   4

a4             =   d+    fs3            =  20+    rectan         =  1c

a5             =   6+    fs4            =  10+    relab1         =  3a

actint         =   e     ftbase         =   0+    relabs         =  38

alkeys         = 214+    ftbyte         =   3+    rest             a60+

as0            =  d4+    ftfsx          =   1+    restor         =  2e

as1            =  6a+    ftfsy          =   2+    save           =  2c

as2            =  34+    ftpth          =   6+    schedr         =   c

as3            =  1a+    ftptl          =   5+    screen         =   0+

b0             =  c8+    ftysiz         =   4+    scroll         =  30

b1             =  64+    g0             =  fd+    scrstr         =  16

b2             =  31+    g1             =  7e+    sct0           =   1+

b3             =  18+    g2             =  3e+    sct1           =   2+

bcdadd         =  62     g3             =  1f+    sct2           =   3+

bcdchs         =  6a     g4             =   f+    sct3           =   4+

bcddiv         =  68     g5             =   7+    sct4           =   5+

bcdmul         =  66     g6             =   3+    sct5           =   6+

bcdneg         =  6c     g7             =   1+    sct6           =   7+

bcdsub         =  64     g8             =   0+    sct7           =   8+

begram         =4fce     gamstb         =4ff8+    semi4s         =4fde+

bitspl         =  a0+    getnum         =  4e     senflg         =4ffa+

blank          =  2a     getpar         =  4c     sentry         =  42

bmusic         =  12     gs0            =  ee+    setb           =  7a

bytepl         =  28+    gs1            =  77+    setout         =  16

c1             =  bd+    gs2            =  3b+    setw           =  7c

c2             =  5e+    gs3            =  1d+    sf0            =   9+

c3             =  2e+    gs4            =   e+    sf1            =   a+

c4             =  17+    gsbend         =   7+    sf2            =   b+

c5             =   b+    gsbscr         =   1+    sf3            =   c+

c6             =   5+    gsbtim         =   0+    sf4            =   d+

c7             =   2+    gtmins         =4fee+    sf5            =   e+

cba            =   9+    gtsecs         =4fed+    sf6            =   f+

cbb            =   7+    horaf          =   f+    sf7            =  10+

cbc            =   6+    horcb          =   9+    shiftu         =  60

cbd            =   5+    humanr         =  40     sj0            =  15+

cbe            =   4+    incscr         =  54     sj1            =  17+

cbflag         =   8+    indexb         =  5c     sj2            =  19+

cbh            =   b+    indexn         =  56     sj3            =  1b+

cbixh          =   3+    indexw         =  5a     skyd           =  13+

cbixl          =   2+    infbk          =   d+    skyu           =  12+

cbiyh          =   1+    inlin          =   f+    sndbx          =  18+

cbiyl          =   0+    inmod          =   e+    snul           =   0+

cbl            =   a+    intpc          =   0     sp0            =  1c+

chdown         =   1+    intst          =   8+    sp1            =  1d+

chleft         =   2+    jmpd             58a+    sp2            =  1e+

chrdis         =  32     kctasc         =  40     sp3            =  1f+

chrigh         =   3+    key0           =  14+    ssec           =  11+

chtrig         =   4+    key1           =  15+    st0            =  14+

chup           =   0+    key2           =  16+    st1            =  16+

Feb 08 16:23 2002	**  Symbol Table  **	 Page 17

cnt            =4fdd+    key3           =  17+    st2            =  18+

col0l          =   4+    keysex         =4fe3+    st3            =  1a+

col0r          =   0+    legsta           a3d+    stimer         = 200+

col1l          =   5+    magic          =   c+    storen         =  58

col1r          =   1+    master           821+    strdis         =  34

col2l          =   6+    math           =  56     suck           =   c

col2r          =   2+    mc               4b8+    sw0            =  10+

col3l          =   7+    mcall          =   6     sw1            =  11+

col3r          =   3+    menu           =  4a     sw2            =  12+

colbx          =   b+    menust         = 218+    sw3            =  13+

collst         =4fe8+    mjump          =   a     sysram         =9fcd+

colset         =  18     move           =  5e     syssuk           376+

concm          =   8+    mret           =   8     system           309+

crel             9d8+    mrflop         =   6+    textd            5ef+

cs1            =  b2+    mrlock         =4ff7+    timout         =4fec+

cs2            =  59+    mror           =   4+    tmr60          =4feb+

cs3            =  2c+    mrrot          =   2+    tonea          =  11+

cs4            =  15+    mrshft         =   3+    toneb          =  12+

cs5            =   a+    mrxor          =   5+    tonec          =  13+

ct0            =4fd5+    mrxpnd         =   3+    tonmo          =  10+

ct1            =4fd6+    msktd          =  7e+    umargt         =4ffb+

ct2            =4fd7+    muzak          =  12     upistr         =   0

ct3            =4fd8+    muzpc          =4fce+    usertb         =4ffd+

ct4            =4fd9+    muzsp          =4fd0+    vbblnk         =   6+

ct5            =4fda+    mxscr          = 21e+    vbcchk         =   4+

ct6            =4fdb+    negt           =  74     vbch           =   3+

ct7            =4fdc+    nogame         = 235+    vbcl           =   2+

ctimer         = 203+    noplay         = 228+    vbclat         =   3+

d1             =  a8+    normem         =4000+    vbclmt         =   0+

d2             =  54+    note1            65e+    vbcrev         =   1+

d3             =  29+    note2            699+    vbdch          =   1+

d4             =  14+    note3            6e6+    vbdcl          =   0+

dabs           =  72     note4            73d+    vbdxh          =   4+

dadd           =  6e     note5            7a6+    vbdxl          =   3+

deccts         =  10     numply         =4ff3+    vbdyh          =   9+

def2               0+    nwhdwr         =   1+    vbdyl          =   8+

def3              33+    oa1            =  8f+    vblank         =  28

def4              97+    oa2            =  47+    vbmr           =   0+

def5              ee+    oa3            =  23+    vboah          =   e+

def6             195+    oa4            =  11+    vboal          =   d+

def8             210+    oa5            =   8+    vbsact         =   7+

disnum         =  36     ob0            =  fe+    vbstat         =   1+

distim         =  52     oc0            =  f1+    vbtimb         =   2+

do               474+    od1            =  d6+    vbxchk         =   7+

doit           =  44     oe1            =  bf+    vbxh           =   6+

doitb          =  46     of1            =  b4+    vbxl           =   5+

dont             497+    og1            =  a0+    vbychk         =   c+

ds1            =  9f+    opot0          =4fdf+    vbyh           =   b+

ds2            =  4f+    opot1          =4fe0+    vbyl           =   a+

ds3            =  27+    opot2          =4fe1+    vect           =  3e

ds4            =  13+    opot3          =4fe2+    vectc          =  3c

ds5            =   9+    osw0           =4fe4+    veraf          =   e+

ds6            =   4+    osw1           =4fe5+    verbl          =   a+

dsjnz            a08+    osw2           =4fe6+    vibra          =  14+

dsmg           =  70     osw3           =4fe7+    voicem           927+

durat          =4fea+    output           855+    voices         =4fd4+

Feb 08 16:23 2002	**  Symbol Table  **	 Page 18

e1             =  96+    paws           =  50     volab          =  16+

e2             =  4a+    pizbrk         =  48     volc           =  15+

e3             =  25+    pot0           =  1c+    voln           =  17+

e4             =  12+    pot1           =  1d+    volume           991+

emusic         =  14     pot2           =  1e+    vwritr         =  1e

endscr         =4ff4+    pot3           =  1f+    waste          = fff

endx           =  c0+    prior          =4ff9+    waster         = fff+

exit             43f+    pswcy          =   0+    writ           =  24

f1             =  8d+    pswpv          =   2+    writa          =  26

f2             =  46+    pswsgn         =   7+    writp          =  22

f3             =  22+    pswzro         =   6+    writr          =  20

f4             =  11+    pushn            95b+    xintc          =   2

f5             =   8+    pvolab         =4fd2+    xpand          =  19+

fill           =  1a     pvolmc         =4fd3+    xpndon         =   1+

fillq            3e4+    quiet            a95+    xyrell           2cf+

firstc         =2000+    quit           =  78